## Slide 1
Francis Perez
September 8th, 2022
X AUSE Conference & V ALBA User’s Meeting
ALBA II Accelerator Upgrade Project

## Slide 2: Objective
Upgrade the 3rd Generation ALBA Storage Ring
to a 4th Generation Ultra Low Emmittance Ring: ALBA II
with the aim of doing the it as efficiently as posible,
in terms of cost and time.

## Slide 3: Optimization parameters
Keep beam energy 3 GeV
Keep the tunnel  SR with similar compact circumference
Keep existing ID beamlines  preserve 16 cells and source points
Bending beamlines can be relocated
Keep injector (present εxbooster = 10 nm∙rad)
Keep infrastructures, as much as possible
Straight sections 4 m, with βx βy 2 m
Reduce emittance by more than a factor 10 (<400pmrad)

## Slide 4: Present lattice

## Slide 5: Proposed solution
From 2x8 double-bend lattice
to 16 multi-bend lattice (6BA)

## Slide 6
The 6BA lattice
At ALBA II ID position,
with 100% coupling, almost round beam:
sx = 14.0 um s’x = 7.1 urad
sy = 15.1 um s’y = 6,6 urad
High beta
required
for Injection
1/4
At ID position, today:
sx = 127 um ; s’x = 47 urad
sy = 5.2 um ; s’y = 4,4 urad
At ID positions, with 100% coupling,
almost round beam
4 fold symmetry
Transversal beam size comparison:

## Slide 7: Comparison of some ALBA IDs
Brilliance Horizontal Coherent fraction
vs. Photon Energy
100 eV 1 keV 10 keV
100 eV 1 keV 10 keV

## Slide 8
Straigth sections for IDs
308 mm
308 mm
308 mm
But 3 will be used for
the Accelerator:
1 for Injection
2 for RF
With high betas (bx=11,7 ; by=10,0)

## Slide 9: Implementation
Possible long beamlines at BL02-ID , BL03-Bend, BL04-ID, BL08-ID

## Slide 10
Straight | BL |  | Comments
SR01 | 2 | FREE | 
SR02 | 4 | MSPD | 68mm displacement
SR03 | 6 | XAIRA | 
SR04 | 8 | FREE | 308mm displacement / Large Beta
SR05 | 11 | NCD | 
SR06 | 13 | XALOC | 68mm displacement
SR07 | 15 | 3SBar | 
SR08 | 17 | RF | & Pinhole3
SR09 | 20 | LOREA | 
SR10 | 22 | CLAESS | 68mm displacement
SR11 | 24 | CIRCE | 
SR12 | 26 | RF | 
SR13 | 29 | BOREAS | 
SR14 | 31 | FAXTOR | 68mm displacement
SR15 | 33 | FREE | 
SR16 | 0 | INJECTION | 
3x FREE
10x IN USE
3x ACCELERATOR
ID Ports
BM | BL |  | SuperBend | Comments
SR02_QD_3 ? | 1 | MIRAS |  | 
SR02_QD_1 | 3 | FREE | Ok | 
SR03_QD_1 | 5 | FREE |  | Limited space due to MSPD
SR04_QD_2 | 7 | FREE |  | 
SR05_QD_1 | 9 | MISTRAL |  | 
 | 10 | Blocked |  | NCD
 | 12 | Blocked |  | Xaloc
SR07_QD_2 | 14 | FREE |  | 
SR08_QD_2 | 16 | NOTOS | Ok (-2.5º) | Superbend requires to move BL 480mm
 | 18 | Blocked |  | Truck entrance
SR09_QD_4 | 19 | FREE | Ok | 
 | 21 | Blocked |  | CLAESS – Used for Pinhole2
SR11_QD_2 | 23 | FREE |  | 
SR12_QD_2 | 25 | MINERVA |  | 
 | 27 | Blocked |  | eALBA
SR13_QD_3 | 28 | FREE | Ok | 
SR14_QD_4 | 30 | FREE | Ok | 
SR15_QD_4 | 32 | FREE | Ok | 
 | 34 | Blocked |  | Pinhole1 + Xanadu
9x FREE
4x IN USE
6x BLOCKED
Bending Ports

## Slide 11
Magnets
  ∼ 600 magnets
  With power supplies
  Some, permanent magnets?
Vacuum chambers
  ∼ 270 m vacuum chambers
  SS, Cu, NEG coated
Girders
  High vibration modes
  High precision remote movement
Many others:
  Upgrade RF system with SSA and 3rd Harmonic Cavity
  New Diagnostics equipment
  New Insertion Devices
  …
Implementation

## Slide 12: ALBA II Enabling Technology Project
The Ministry gave CELLS a grant of 7.5 M€, for “the development of advanced technologies for ALBA II”.

## Slide 13
ALBA II Enabling Technologies
2022- 2025
Design and prototype construction of
  Magnets
  NEG Coated vacuum chambers
  Pulsed magnets
  Girder for arc assembly tests
Nano-positioning lab
Superconducting Undulator

## Slide 14
ALBA II Enabling Technologies
2022- 2025
The structure of project has been implemented such that will fit in the future ALBA II structure

## Slide 15
WP1 - Magnets
ALBA II Enabling Technologies Project
Magnets design
Prototypes definition
3) Upgrading the Mag Lab

## Slide 16
WP2 - Vacuum
ALBA II Enabling Technologies Project
Reviewed requirements
First layout considerations
3) Stablishing collaborations with Max IV

## Slide 17
WP3 – Pulsed Magnets
ALBA II Enabling Technologies Project
Design done: Novel topology adopted  Double Dipole Kicker (DDK)
Call for tender published in July
3) Stablishing collaboration with SIRIUS

## Slide 18
WP4 - Girders
ALBA II Enabling Technologies Project
Preliminary Research: evaluating alternatives from other projects.
First general concept designs

## Slide 19
WP5 – Nanoposition Lab
ALBA II Enabling Technologies Project
Working on:
  Spaces definition and detailing
    Construction solutions
    Services & Network
    Conventional and Mechanical installations
  Material:
    Furniture, benches, tools, tooling list…
  Instrumentation and controllers definition

## Slide 20
WP6 – Superconducting Undulator
ALBA II Enabling Technologies Project
Reviewing state of the art.
Analyzing best case for ALBA II requirements.

## Slide 21: Conclusions
ALBA II is feasible:
  emmittance ∼ 150 - 200 pmrad
  betas X,Y ∼ 2.0 - 2.5 m
Up to 26 beamlines are feasible:
  13 IDs
  13 Bendings
    Some of these bending positions can be used for up to 3T superbend.
Prototyping for the Acceleraror Upgrade has started.

## Slide 22
X AUSE Conference & V ALBA User’s Meeting
Thanks!
September 8th, 2022

## Slide 23: Beam sizes at emission points

## Slide 24
The 6BA lattice has a
main bending of 1T (<1,4T of ALBA)
Propose to add:

## Slide 25
Bendings emission comparison
1 T
3.2 T
For beamlines Eph ≲ 2 keV
it is more favorable the 1T bending

## Slide 26: Possible sources
13 IDs
  12 small betas
  1 high betas
13 bendings
  Keep the bending beamlines MISTRAL & MINERVA with 1T bending
  Move NOTOS to a 3T bending
  4 more possible with 1T bending
  5 more possible with either 1T or 3T bending
MIRAS
  Could be maintained in the same position, but the mechanical desing of the extraction from the SR has to be investigated.

## Slide 27: Accelerator’s Investment
2022 - 2029