## Slide 1: Cell imaging at ALBA Current and proposed techniques
Judith Juanhuix
06.10.2021
Slides from:
Tanja Ducic
Alberto Mittone
Eva Pereiro
Ana Pérez-Berná
Andrea Sorrentino

## Slide 2: Biological imaging techniques today
cryo-3DSIM
Cellular Biology Interactomics Macromolecules
VLM
cryo-SXT
resolution
Multimodal imaging across resolution scales is essential to understand biological mechanisms.
1 Å
500 nm
5 nm
30 nm
sample thickness
cryo FIB-SEM
5 µm
µPCXT
µFTIR
cryo-ET
Single Particle
Tissue
Organoids
nanoXRF
cryo-SR
operational
in development
out of Alba
nanoPCXT
MX
BioSAXS
NMR
subPCXT
subXRF
Notes: Lab-grown mouse mammary gland imaged by 3D confocal (Dr. Harris Univ. Cambridge)

## Slide 3
 | cell sub-10 nm | cell sub-100 nm | tissue sub-100 nm | tissue 100-500 nm | Tissue/cells 1-5 µm
3D structure | --- | SXT | holotomography | phase contrast tomography ptychotomography+ | phase contrast tomography
2D chemical info | --- | XANES |  | XANES | µFTIR
3D chemical info | --- | spectro-tomography*, edge enhanced tomography |  |  | 
2D elemental quantification (ppm) | --- | XRF |  | XRF | 
3D elemental quantification (ppm) | --- | XRF |  |  | 
Sample conditioning | cryo | cryo | HPFreezing/cryo with embedded samples# | cryo/RT | RT
Synchrotron-based imaging at 3rd
and 4th generation sources
* dose limitation slow techniques
+ difficult for users # sample shrinking in the beam
3D XRF & ptychotomography slow: 1 tomo/day

## Slide 4: Current tools in Structural Cellular and Tissue Biology at ALBA
XALOC (MX)
NCD-SWEET
(SAXS)
XAIRA (mMX)
CryoEM-SPA (200kV)
BioLabs
MIRAS (IR)
MISTRAL (TXM)
FAXTOR (HXT)
Fully
dedicated
Partially
dedicated
In
construction
Facilities in Structural
Cell Biology:
MIRAS (IR bl)
MISTRAL (TXM, full field, soft XR)
FAXTOR (HXTomo)
CLAESS (XANES)
Molecular
Biology
Residual
use

## Slide 5: MISTRAL beamline: Soft X-ray Tomo
TXM (Transmission X-ray Microscope) capability :
  2D Measured Spatial Resolution ≈ 30 nm half pitch.
  Detector effective Pixel size 16 nm – 8 nm, Field of view 8x8 µm2 - 16x16 µm2.
  Cryo environment ( ≈ 110 K).
  On-line visible light epifluorescence microscope for correlative low resolution 2D imaging.
Available techniques for bio-samples (with 30 nm spatial resolution):
  Cryo – soft X-ray Tomography (± 70◦ max angular range, typical acquisition time ≈ 5 -10 min.).
  Cryo – X-ray Spectromicroscopy (from Ca L – edge).
CCD
sample
capillary condenser lens
central stop
objective zone plate lens
(40nm and 25 nm ZP)
Notes: ≈109 Gray.
5 BLs like Mistral (Mistral was the 3rd one).

## Slide 6
What we do now at MISTRAL
Identifying specific cellular structures
Follow processes
Evaluating cellular morphological changes
only 2D low resolution VLM
correlation in cryo… still.

## Slide 7
In-house program: Structural info of infectious diseases
Hepatitis C infection
Assessment of the reversion of HCV-induced cellular ultrastructural changes direct-acting antiviral drugs

## Slide 8
Study of SARS-CoV-2 infection and therapy causing intracellular membrane alterations
Characterisation of structural alterations induced by Zika virus
Integrated Structural Biology Study of Mycoplasmas
Barbara Machado
XALOC BL
Damia Garriga
XAIRA BL
Sample preparation strategies for efficient correlation of cryo 3D-SIM and soft X-ray tomography
In-house program: Structural info of infectious diseases
Ana Pérez
MISTRAL BL
Ana Pérez
MISTRAL BL

## Slide 9
Cancer research
Chemotherapy
hyperthermia in tumor cells
Mitochondrial dysfunction
Chromatin expression
Cell biology at MISTRAL
38%
19%
5%
Immune systems
Cholesterol
T-Cell Migration
T-Cell interaction with pathogens
Primary T-cells
10%
Pathogens
HCV
Zika
Mycoplasma
SARS-CoV-2
Plasmodium Falciparum
Babesia divergens
Herpes
Torovirus
Vaccinia
Bio mineralization
Cholesterol
Calcium
Hydroxyapatite
21%
Alzheimer
E. Coli
SARS
Cytomegalovirus
Rotavirus
Trypanosome Brucei
Influenza
Mycoplasma
Nanoparticle:
hyperthermia in tumor cells
Gold coated siRNA
Anti-inflammatory events
Drug delivery
Nano liposomes
1%

## Slide 10
What we’ll be doing soon: 3D cryo CLXM
Identifying specific cellular structures
Follow processes
Evaluating cellular morphological changes
cryo 3D-SIM correlated to cryo-SXT
NIH-3T3 cells
2D X-ray mosaic & SXT
2D X-ray mosaic
primary fibroblats
3D SIM & SXT
2D mosaic & 2D SIM
All users groups will benefit!

## Slide 11
Ongoing at Mistral & Miras… and new!
?
cryo-SXT
SR-µFTIR
cryo
nano-XRF
cryo-3D-SIM
cryo
epifluorescence
cryo
nano-XANES
operational
in development
out of Alba
new
cryo-ET
cryo FIB-SEM
PCXT
XANES
XRF
protocols demonstrated on system models

## Slide 12
5 µm
5 µm
1 µm
2 µm
J.J Conesa et al. Angew. Chem. 1270-1278 (2020)
Example of
cryo-SXT correlated to
3D cryo XRF
Example of cryo-SXT
correlated to SR-µFTIR
control
HCV replicating cells
lipids
amide I
oxidation
cryo-SXT
Pérez-Berná et al. (in press)
…in addition to cryo 3D-SIM

## Slide 13: MISTRAL User support
Cell culture Platform
Vitrification Platform
Sample screening at cryo
MISTRAL BEAMTIME
Data Processing support
Asistance to the user during the beamtime from 8:00 to 20:00
Notes: The idea is to expand the capabilities of this services

## Slide 14: MIRAS BL (FTIR) Current work on Alzheimer disease
Synchrotron X-ray Fluorescence and FTIR signatures for Amyloid Fibrillary and non-fibrillary Plaques.
Álvarez-Marimon et al., ACS Chem. Neurosci. 2021

## Slide 15: Multimodal synchrotron-radiation approach combining FTIR, hard and soft X-ray microscopy on intact astrocytes from a rat model of Amyotrophic Lateral Sclerosis (ALS) disease
Ducic et al, Analytical Chemistry 2019
MIRAS BL (FTIR) Current work on Amyotrophic Lateral Sclerosis

## Slide 16
TOWARDS INTEGRATIVE IH PROJECTS
Organic and elemental correlative imaging by using synchrotron light for illuminating molecular disorders in neuro diseases
Ducic et al., Microscopy and Microanalysis 2021
Soft X-ray tomography
FTIR
X-ray
fluorescence
Invited talk to Microscopy and Microanalysis 2021
organized by Microscopy Society of America
doi:10.1017/S1431927621000982

## Slide 17: Techniques and science at FAXTOR (CT)
Available techniques:
X-ray phase contrast imaging
X-ray absorption imaging
Time resolved radiography
Computed tomography (3D/4D)
+ Material science, Paleontology and cultural heritage, Earth and Planetary Sciences...
+ Combination with external stimuli
land
G. Barbone et al. IJROBP, 2018.
Micro-imaging of Brain Cancer Radiation Therapy Using Phase-contrast Computed Tomography.
In-situ visualization of sound-induced otolith motion using hard X-ray phase contrast imaging.
T. Schulz-Mirbach et al, Sci. Rep, 2018.
Multiscale X-ray phase contrast imaging of human cartilage for investigating osteoarthritis formation.
A. Horng et al, J. Biomed. Sci, 2021.
Notes: As techniques propagation based X-ray phase-contrast and absorption-based imaging will be used on a daily basis. Future extensions including differential phase-contrast imaging can be also foreseen. Different acquisition protocols will be available, from time resolved projection imaging, to static and time resolved computed tomography.

## Slide 18: Current status of the Life Sciences tools
From Harkiolaki et al. DOI:10.1042/ETLS20170086 ; CC BY 4.0 modified
SAXS
1 nm
FAXTOR
XALOC
XAIRA
There is a resolution gap between molecular and cell biology to be filled
To become “catalist for health and environment” requires more tools and services
MISTRAL
FTIR
3 mm
MIRAS

## Slide 19: New tools to fill in the gaps
From Harkiolaki et al. DOI:10.1042/ETLS20170086 ; CC BY 4.0 modified
BioSAXS
1 nm
FAXTOR
MISTRAL
XALOC
BioSAXS
XAIRA
STXM
Cry-EM/SPA
MIRAS
Computational
Biology
New tools based on different probes required: XR, visible light, electrons, IR
Aiming at a continuous path from genotype to phenotype structural studies
ALBA embedded within their strategic partners provides leading capabilities
Correlative Microscopies
Visible Li
Notes: Eva: visible light FLUORESCENCE
“nanoprobe”: Holotomography full field + STXM

## Slide 20: Proposed tools in Structural Cell and Tissue Biology
Existing
tools
Proposed
tools
CryoET
BioLabs
New tools proposed in Cell and Tissue Biology:
2 new hard XR BLs, 1 new branch
nanoIR facility
Correlative microscopies
CryoET
Computational Bio
MIRAS (IR)
MISTRAL (SXT)
FAXTOR (HXT)
Cryo nanofocus 3D
(fluo+phase contrast)
High energy CT
Cryo3D-SIM
sub-mm CT
nanoIR
CryoFIB-SEM
Notes: Green: have it
Yellow: in construction
black: we are proposing
Red: simply NO
Upgrade to THz in the beamline

## Slide 21: Cryo-Electron Tomography
Suitable for visualizing organelles and cell ultrastructure
Solves structures in situ, and mixed populations
Bridges the gap between structural molecular and cellular biology
Requires:
  Sample preparation lab
  Screening electron microscopes
  Correlative cryo super-resolution microscopies for best results
Cryo-EM (Tomo, also SPA) facilities often associated to Synchrotrons
  Similar sample prep to other techniques
  Similar user community
Need to coordinate with CNB national facility for electron microscopy
FEBS Letters, 594:20, 2020
DOI: 10.1002/1873-3468.13948
Data integration from molecules to cells.
Tomographic slice of a C. crescentus cell.
(B) The in situ molecular organization of the Golgi apparatus from C. reinhardtii.
(C) Molecular sociology within poly‐Gly‐Ala aggregates shows an increased concentration of 26S proteasomes.
Notes: Examples of in situ cryo‐ET application. (A) Data integration from molecules to cells. A tomographic slice of a C. crescentus cell showing the inner membrane (IM), outer membrane (OM), and surface layers (S‐layer). The 4.8 Å in situ cryo‐ET sub‐tomogram averages (gray) of the S‐layer lattice are mapped back into the tomogram, and structures from X‐ray crystallography at 2.7 Å (red) and single‐particle averaging at 3.7 Å (blue) are docked. The inset (right) illustrates an integrative model of the S‐layer anchoring into the outer membrane, combining structural and native MS methods. For comparison, the inset (left) shows an early electron crystallography map of the S‐layer ring structure at 2 nm resolution [124]. (B) The in situ molecular organization of the Golgi apparatus from C. reinhardtii. A tomographic slice containing the cisternae stacks of the Golgi apparatus (left) and its segmented representation (right) revealing the cis (green), medial (magenta), and trans (blue) cisternae and COPI vesicles as well as the morphology of the endoplasmic reticulum (ER, yellow), trans Golgi network (TGN, purple), and two nuclear pore complexes, ribosomes, and other membranes (gray). In the tomographic slice, several COPI‐coated vesicles and those budding off are indicated by asterisks. The inset shows the molecular architecture of the ex situ COPI‐coated vesicle. (C) Molecular sociology within poly‐Gly‐Ala aggregates shows an increased concentration of 26S proteasomes. A tomographic slice (left) of a neuron expressing poly‐Gly‐Ala repeats. Mapping of macromolecules near the periphery of an aggregate region (right) shows 26S proteasomes in the ground state (GS, green) and an enrichment for the substrate‐processing state (SPS, blue) proximal to poly‐Gly‐Ala twisted ribbons (red). Other molecular species, such as the ribosomes (yellow) and the chaperonin TRiC (purple), are largely excluded from the aggregate material. The inset shows a closeup of two 26S proteasome sub‐tomogram averages after classification revealing the non‐processing GS and the engaged SPS. Figure (A) inset (left) reproduced from Ref. [124].

## Slide 22: Cryo-nano XR Fluorescence and phase-contrast imaging
Nanofocus beamline with a scanning transmission X-ray cryo-microscope
  Nanofluorescence: quantification of trace endo- and exogenous elements at high-sensitivity
  Phase contrast-based imaging: 2D and tomography of cells
Addressed community: Cell Biology, Metallobiology, drug delivery, nanomedicine, applied nanomaterials, new therapeutic agents, genetic recessive diseases, viral infections, biocatalysis.
Required: spatial stability in cryo conditions, isometric aspect ratio, flux at focus
Desirable: coherence for near-field ptychography and holotomography.
Open questions: Energy range? Resonant energies for scanning specific oxidation states?
Similar beamlines: ID16A@ESRF, I14@Diamond, P06@DESY (cryogenic condition to be installed), Nanoscopium@SOLEIL, NanoMAX@MAXIV (no cryogenic conditions)

## Slide 23: Non-SR Microscopies
Cryo-3DSIM
Used as a preferred correlative microscopy for SR techniques
Only 2 units worlswide: Diamond and ALBA
Sample preparation lab required
Screening microscopes required
Key to correlate images from external optical labs to images from SR-based techniques
CryoFIB-SEM
Imaging of cryo-sectioned cells and tissues
Resolution down to 30 nm
Long acquisition time
Common sample preparation with other techniques
MF Hayles, DAM de Winter, DOI: 10.1111/jmi.12951

## Slide 24: Map of existing, in construction and proposed tools
BioLab
Proteomics
BioSAXS BL
Cryo-EM
(Single Particle Analysis)
XALOC BL
(HT MX, jet SSX)
MIRAS BL
(FTIR)
Biolab
Mammal cell lab
FAXTOR BL
(HXR and sub-m CTomography)
XAIRA BL
(m-MX, fixed-target SSX)
BioMed BL
(HE CT)
nano-IR
Cryo-3D SIM
Resolution
Standardization
existing
proposed
In construction
BioLab
Sample prep (P2)
MISTRAL
(SXR Transmission Tomo)
Cryo-EM
(Electron Tomography)
Cryo FIB-SEM
Cryo nano-XRF BL

## Slide 25: The Conclusion
 | FTIR live cells | nano IR | Cryo SXT | Cryo XRF | Cryo ET | Cryo 3D-SIM | CryoFIB-SEM | Sub-mm CT | HE CT in vivo
 | IR | IR | Soft X-rays | Hard X-rays | Electrons | Visible | Electrons | Hard X-rays | Hard X-rays
 | SB | SB/FEL | SB | U |  | - | - | SB/W | SB/W
 | Far IR | Near IR | 280-3000 eV | 10-25 keV | (300 kV) | - | - | 20 keV | 30-120 keV
 | 100 mm | 10 nm | < 25nm + unfocus | <100nm + unfocus | - | - | . | <1- µm | 500-50 nm
Near Native |  |  |  |  |  |  |  |  | 
Multimodal |  |  |  |  |  |  |  |  | 
Time-resolved |  |  |  |  |  |  |  |  | 
4th generation upgrade
3th generation upgrade
essential tool
Desirable tool
Capability
Notes: Tanja, Ibreheem: feed for FTIR live cells. Diffraction limit? Useful for Life Sciences???
Weakness: 0.5 um microXRF