## Slide 1: Permanent Magnets at STFC
Ben Shepherd
2nd PerMaLIC Workshop
ALBA
3 November 2022

## Slide 2: The ZEPTO concept
Shepherd et al, IPAC2014 TUPRO113
Zero-Power Tuneable Optics
Highly adjustable PM quadrupole and dipole magnets to replace electromagnets
  Large tuning range using motors to move PMs
  Same physical footprint
  No energy usage (except a tiny amount when adjusting)
  Less infrastructure required (no big current cables, power supplies, cooling)
Prototypes built at Daresbury: 2 quads, 1 dipole
  27 mm aperture (40 mm for dipole)
  230 mm length
  15-60 T/m, 4-35 T/m, 0.55-1.1 T ranges
  Fixed steel poles, movable NdFeB PMs
  Simple control system with one motor
Q1
Q2
D1

## Slide 3
ZEPTO @ Diamond Light Source
ZEPTO technology is applicable anywhere that adjustable DC magnets are required, and can be used as an energy saving `drop-in' replacement for electromagnets on accelerators such as existing light sources.
We have developed a new ZEPTO quadrupole for the booster-to-storage ring section of Diamond Light Source.
0
0.2
0.4
1.2
0.8
1.0
0.6
1.4
0.2
0.4
1.2
0.8
1.0
0.6
1.4
Contours B (T)
Slide: Alex Bainbridge

## Slide 4
OPERA 3D model
SmCo blocks attached to vertical motion system with 90mm movement range and 1 µm precision
Fixed “inner yoke” defines the quadrupole field
Fixed “outer yoke” can steer flux away from the beam, allowing the gradient to be adjusted
No magnetic contact between yokes, the gap between is filled with aluminium for rigidity
Simulations predicted a gradient tuning range from 23 T/m down to 0.35 T/m
The outer yoke acts as a short circuit for the flux, allowing the magnet to be ‘turned off’.
ZEPTO-Q3
32 mm aperture
Slide: Alex Bainbridge

## Slide 5
Previous ZEPTO magnets used large NdFeB blocks to produce the magnetic flux, which are difficult to manufacture and handle.
New magnet uses a “carriage” with a number of smaller blocks set into an aluminium latticework.
Advantages over larger single blocks which include:
Blocks are easier and cheaper to manufacture.
Damaged single blocks may be replaced instead of the entire carriage.
Variation in block BH curves may be compensated.
Modular magnet "families" may be created by strategic removal of blocks.
The gaps between blocks do not affect field quality as the flux must pass through a steel pole before reaching the beam.
We use SmCo instead of NdFeB for improved radiation hardness and temperature stability.
No thermal shunts are needed
Permanent magnets
300 mm
33 mm
50 mm
Slide: Alex Bainbridge

## Slide 6
In previous ZEPTO quadrupoles field measurements revealed the magnetic centre moving as function of magnet block position, mostly vertically, due to unexpectedly magnetic components.
Expecting this, each magnet carriage now has a dedicated motor and associated driving ball screw to help compensate.
Look-up table can be applied to either carriage position to compensate and restore the magnetic centre to the geometric centre.
Dual motor system
Shepherd et al, IPAC’14, Dresden, Germany, paper TUPRO113.
Motor
PM Carriage
Ball screw
Carriage holder
Slide: Alex Bainbridge

## Slide 7
Split design
Electromagnetic quadrupoles can typically be split for installation around an existing vacuum vessel – previous ZEPTO quadrupoles could not.
The new version may be split about the vertical axis and reassembled around an existing vacuum system using a dedicated assembly frame.
This allows replacements or repair to be conducted without needing to keep the accelerator offline for the additional time needed to restore the quality of the vacuum.
Vacuum chamber
Temporary PM carriage holder
Pre-bolted inner and outer yokes
Yoke supports
Rail
Slide: Alex Bainbridge

## Slide 8
Split design
Electromagnetic quadrupoles can typically be split for installation around an existing vacuum vessel – previous ZEPTO quadrupoles could not.
The new version may be split about the vertical axis and reassembled around an existing vacuum system using a dedicated assembly frame.
This allows replacements or repair to be conducted without needing to keep the accelerator offline for the additional time needed to restore the quality of the vacuum.
Slide: Alex Bainbridge

## Slide 9: ZEPTO-Q3 installation
Installation frame
Dummy magnet holder
Frame around pedestal
Bringing in magnet sides
Assemble sides around dummy magnets
Permanent magnet blocks
Place PMs around vacuum chamber
Bring in magnet sides
Magnet sides to meet PMs in centre
Fully assembled magnet
Protective Perspex cover
Installation complete

## Slide 10: ZEPTO vs electromagnet performance
ZEPTO
Minor trajectory corrections after turning ZEPTO up to nominal field
Injection efficiency returned to normal level (70%)
Now running in user mode with top-up injection
Beam shape on screen for same field:
EMQ
ZEPTO

## Slide 11: HEPTO: coil-adjustable PMs for light sources
ifast-project.eu
Slide: Alex Hinton
Hybrid Electro-Permanent Tuneable Optics
Central dipole field: 0.695 T
Central gradient: 32.4 T/m
Magnetic length: 0.870 m
Integrated dipole field: 0.605 Tm
Integrated gradient: 28.2 T
Good field region radius: 7 mm
Field quality ΔB/B within GFR: 5x10-4
Gradient quality ΔG/G within GFR: 1x10-3
Integrated multipoles < 10-3
Integrated field quality < 10-4
Dipole tuning range: ±2.5%
Gradient tuning range: ±2.5%

## Slide 12: ECRIS: adjustable PM dipole for ion sources
Compact ion source applicable to
  Thin Films centre
  Materials characterisation at ISIS
Includes PM-based m/q separator
  Simpler than traditional EM-based system
Mechanical adjustment: 65-87 mT
Assembled and tested at DL in 2022
Excellent agreement with modelling
Field quality 5x10-4
Olli Tarvainen et al, Nuclear Physics B (2022), in press

## Slide 13: Shimmable Hybrid Halbach quadrupoles for EPAC
EPAC is the Extreme Photonics Application Centre, currently under construction at RAL
ASTeC is responsible for designing an electron beamline to capture an electron bunch accelerated in a Laser Plasma system
High divergence bunches with energies from 100 MeV to several GeV are anticipated
To capture and focus the bunches, a beamline comprising 10 high strength fixed gradient small aperture quadrupoles is proposed
Peak Gradient | 500 T/m
Physical Length | 50 mm
Integrated Gradient | > 25 T
Internal Radius | 4 mm
Slide: Neil Thompson
Poles: 1006 Steel
PM Blocks: VACODYM-764-TP
NdFeB, Br 1.37 T
3 insertable tuning rods for each pole: 1006 Steel
Rod-1
Rod-2
Rod-3
Vacuum pipe
Inner radius 4.0 mm
Outer radius 4.5 mm
Rod | ΔG
1 | 4 T/m
2 | 8 T/m
3 | 16 T/m

## Slide 14: Assembly of Halbach quadrupole
Assembly tooling
Hand wheel
Gearbox
Linear guides and leadscrew
Magnet block holder assembly
Remove aluminium spacer to enable magnet assembly
Set base block position and lock into position with pin in indexing feature
Magnet block
Magnet block holder
Clamping screws
Clamping pads (yellow)
Clamping finger
Magnet block holder assembly
Remove clamping screws
Continue translating magnet block into position by turning screw
Magnet block clamped with clamping finger
Add clamp ring and remove clamp fingers
Slide: Clive Hill

## Slide 15: Conclusions
ZEPTO magnets provide a viable highly-adjustable alternative to electromagnets for many accelerator applications
ZEPTO technology is now being used on a user facility
More PM technology is being developed and deployed
Acknowledgments: Alex Bainbridge, Alex Hinton, Olli Tarvainen, Neil Thompson