## Slide 1: Synchrotron Radiation monitors in Hadron Machines
E. Bravin1, S. Mazzoni1, T. Mitsuhashi1,2, M. Palm1, F. Roncarolo1 & G. Trad1
1 CERN Beam Instrumentation group, Geneva (CH)
2 KEK, Tsukuba (JP)
Topical Workshop on Emittance Measurements for Light Sources and FELs, ALBA, 29-30 January 2018

## Slide 2: Outline
SRM for transverse profile:
Imaging
Slit scan
SRM for transverse & longitudinal profile, Halo measurement:
Imaging
Interferometry
(Single photon counting)

## Slide 3: SPS LSS5

## Slide 4: Super Proton Synchrotron
Challenges: bunch by bunch profile measurements over 288 bunch, 25 ns train
Energy: from 26 to 450 GeV in 4.3 s.
Visible SR monitoring: edge radiation extracted to optical system with mirror @ 68 mm from beam axis
SR sent to IMAGING and SLIT SCAN instruments

## Slide 5: SPS BSRT

## Slide 6: SPS BSRT

## Slide 7: SPS BSRT

## Slide 8: SPS BSRT
SR intensity -> g11, detectable > 270 GeV
Typical size: 700 mm (s)
Good radiation tolerance for digital camera. Routinely used in all SPS coast at 270 GeV to monitor emittance change for dynamic studies related to crab cavity test feasibility
fps: 20 (analogue) to 300 (digital): at the limit for single bunch measurement

## Slide 9: SPS slit scan
PMT
500 mm/s
SR
Working
Principle
Profiles
Beam size
Fast moving slits to sample SR beam image
Photons passing through the slit are detected with a photomultiplier tube
Bunch by Bunch beam size in <50 ms => 4 measurements at SPS Flat Top

## Slide 10: SPS slit scan

## Slide 11: SPS slit scan
PMT Voltage [mV]
Samples

## Slide 12: SPS slit scan
This allows BbyB profile reconstruction for emittance estimation

## Slide 13: SPS summary
In 2017, while waiting for SW to exploit the BSRT for routinely beam size measurement in the SPS:
  successfully tested digital cameras
  successfully demonstrated slit scanner as a viable alternative
  Assess whether to invest in a readout system and faster motors to make it operational.
FESA server:
  1st release implementing basic functionalities just saw the light
  to be heavily tested (not possible with beam, only lab).
  development to be continued to reach operational level

## Slide 14: The Large Hadron Collider

## Slide 15: The Large Hadron Collider
LHC Beam parameters [p+] | 
Energy [GeV] | 450-7500
Gamma | 479-7460
Transv. Norm emittance [mm rad] | 3.75
RMS bunch length [ps] | 250
Max number of bunches | 2808
Min bunch spacing [ns] | 25
Bunch population [p+] | 1.1x1011
Approx. beam size at flat top [mm] | 310-400
LHC POINT 4

## Slide 16: SRM in the LHC: source
Undulator
2 periods of 68cm
B= 5 T cte
Dipole
D3, Length = 9.45 m
Bend.angle = 1.58 mrad
Radius curv.= 6 km
In-vacuum extraction mirror
Low Energy : Undulator main Light source
Int. Energy : Undulator + D3 Edge
High Energy : D3 Edge + D3 core

## Slide 17: LHC SR source
PhD thesis of G. Trad
LHC SR power (in units of W/mm2 per proton) at the extraction mirror, for different beam energies
E<800 GeV 1st harmonic emitted by undulator (light cone centred at (0,0))
800 GeV <E<1400 GeV external lobes from undulator radiation
1.4 TeV<E<1.7 TeV Edge light emitting at (0,0)
>1.8 TeV dominating source is the Dipole Core

## Slide 18: LHC SR source
Visible spectrum
SR power (visible)

## Slide 19: LHC BSRT: imaging
BSRT is the only instrument measuring continuously beam size bunch by bunch (not during ramp) in the LHC.
Optical line optimized for 600 nm (injection) and 250 nm (high energy)
BSRT does not provide an absolute beam size, it needs to be cross calibrated w.r.t. Wirescanners (3 in 2017)

## Slide 20: LHC BSRT calibration
Calibrated against wire scanner
M = magnification,
β = beta function at WS and BSRT locations
= b
= point spread function

## Slide 21: LHC BSRT calibration

## Slide 22: BSRT: issues
Clear effect of ageing:
  Reduction of sensor sensitivity, deforming the sensor response.
Mitigation
  Working point optimized to increase I.I. lifetime (attenuate SR input and MCP gain at the cost of SNR)
  Change of working point
  SW compensation of the non uniformity
  Ongoing investigations with Hamamatsu to identify source (photocathode or MCP)
Ageing of the I.I. June
Ageing of the I.I. September

## Slide 23: LHC Intensity and longitudinal profiles
DCCT: Total number of particles in the ring
FBCT: Number of particles per nominal bunch
BSRL: Measure the longitudinal distribution of particles in the LHC with a sufficiently high dynamic range to quantify the relative population in nominally empty buckets.
  Luminosity calibration
  Injection quality
  Origin of background signal at IPs
  Requirements: A dynamic range of 5 orders of magnitude, and a time resolution of 100 ps
Satellites
Ghosts
Satellites
Ghosts
Filled

## Slide 24: LDM layout
Abort gap
monitor
System A
System B
Filters
Filters
Lens
Hybrid
Collimator
BP-filter
Fibre
BSRL
BSRA
Synchrotron light
BSRL+BSRA
BSRT

## Slide 25: LHC LDM principle
Time-correlated single photon counting
Resolution: 50 ps
1.780.000 bins per histogram
5 minutes integration time for 105 dynamic range

## Slide 26: LHC LDM detector and data treatment
Dynamic range > 105
Data correction: availability:
Lab test: LHC-like pulse train (pulsed sub-ns laser)
x100
>105
Raw data
Hybrid
SPAD
Signal level at end of “abort gap”
2.5 ns
Last pulse: raw and corrected data

## Slide 27: R&D instruments: BSRI
Fringe Visibility:
The spatial coherence of the SR is probed by measuring the fringe visibility and calculating the first order degree of mutual spatial coherence Γ at the slits plane
I1
I2
D
R

## Slide 28: BSRI principle
Fixed Slit Separation
(Hyp. Gaussian)
SR Interferometry
The beam size is derived based on the Van Cittert-Zernike theorem, where the degree of coherence Γ is the Fourier transform of the intensity distribution of the source
Inverse Fourier Transformation,
Obtain beam profile
Slit Separation Scanning Mode
  f(x) is obtained by applying an inverse Fourier transf. of the resulting curve Γ(D)

## Slide 29: BSRI layout
Undulator
D3
Beam
Slits
Assembly
Focusing
Lens
f~800mm
Eyepiece
f~30mm
ND & bandpass
Filters
Linear
Polarizer
Intensified
sCMOS
sCMOS sensor
Optical coupling to Image Intensifier
HQ Linear Polarizer (polymer polarizing film between two high-precision glass substrates with flatness better than λ/6) motorized rotational stage allowing IN/OUT movement.
Motorised Apochromat Lens and eyepiece
Slit width and distance can be adjusted

## Slide 30
Bunch 0
Bunch 1785
Slit scan from 3 to 21 mm. Bunch 0 (left), bunch 1785 (right). Emittance blow-up on bunch 1785
BSRI example

## Slide 31
At Flat Top Energy
Beam size from the interferometer larger by a factor of ~1,3.
However, relative bunch by bunch size measured via interferometry is compatible with Imaging.
At Injection Energy
Good agreement with Imaging
Discrepancies with the imaging values are ~5%
BSRI comparison w imaging

## Slide 32: Conclusion
SR monitors present in SPS and LHC
Various experimental challenges: radiation, energy ramp, distance from the source
LHC & SPS BSRS and BSRT routinely used for bunch by bunch emittance measurement
Commissioning of LHC BSRI ongoing. High energy discrepancy w ws and imaging under investigation.