## Slide 1: Overview of the Diamond Light Source
Ian Martin
ALBA Synchrotron Visit
5th October 2017

## Slide 2
Diamond Light Source
general introduction to the facility
different operating modes
top up, low alpha operation
Facility Upgrades / New Beamlines
increasing beam brightness
double mini-beta straight sections
exotic insertion devices
DDBA upgrade
Future developments
DIAD beamline
Diamond II?
Talk Outline
Ian Martin, ALBA Visit, Oct 2017
Diamond Light Source
general introduction to the facility
different operating modes
top up, low alpha operation
Facility Upgrades / New Beamlines
increasing beam brightness
double mini-beta straight sections
exotic insertion devices
DDBA upgrade
Future developments
DIAD beamline
Diamond II?

## Slide 3
Diamond is a 3rd generation synchrotron light source
Located at Rutherford Appleton Laboratory, Oxfordshire, UK
Join Venture between UK Government and Wellcome Trust
Largest UK investment in science for 30 years
Diamond Light Source
Ian Martin, ALBA Visit, Oct 2017

## Slide 4
1993 Woolfson Review: SRS to be replaced by a new medium energy machine
1997 Feasibility Study (“Red Book”) published 3 GeV, 16 cells, 345 m circumference, 14 nm rads
1998 Wellcome Trust joins as partner
Mar. '00 Decision to build Diamond at Rutherford Appleton Lab.
Oct. '00 3 GeV, 24 cells, 560 m circumference design approved
Apr. '02 Joint Venture Agreement signed (UK Govt./Wellcome Trust)
Diamond Light Source Ltd. Established
Design Specification Report (“Green Book”) completed by CCLRC
Jan. '07 Start of Operations
Diamond Light Source
Ian Martin, ALBA Visit, Oct 2017

## Slide 5
Linac (0 to 100MeV)
Booster (100MeV to 3GeV)
Booster to Storage ring (3GeV)
Linac to Booster (100MeV)
Storage Ring (3GeV)
Beam Line
180m
Facility Layout
Ian Martin, ALBA Visit, Oct 2017

## Slide 6
Lattice Double Bend Achromat
Structure 24 cell
Symmetry 6
Straights 18 × 5m / 6 × 8m
Energy 3 GeV
Length 561.6 m
Lifetime >10h
Current 300mA
Emittance 2.7nm.rad
Bunch Length 10ps (3MV)
Energy Spread 9.6x10-4
Main Parameters
Ian Martin, ALBA Visit, Oct 2017

## Slide 7: Overview of Diamond
Beamline Installation
Beamline Installation
35 Beamlines:
29 installed IDs
7 BM beamlines
All straights now occupied
Ian Martin, ALBA Visit, Oct 2017

## Slide 8
3) 156 bunch mode: bunches evenly spread
average current: ~136 mA
bunch spacing: 12 ns
1) Multibunch: bunches spaced by 2 ns, filling 70-90 % of the ring
total current: 300 mA
bunch current: 0.35-0.5 mA (depending on fill pattern)
2) Hybrid: combination of multibunch and single bunch
e.g. 300 mA in consecutive bunches in
2/3rd of the ring + 3.0 nC single bunch
312 ns
312 ns
Injector allows a very flexible fill pattern control, but bunch length limited to >10ps and increases with bunch current.
Several different modes of operation on offer:
Operational Modes
Ian Martin, ALBA Visit, Oct 2017

## Slide 9
Diamond has operated in top-up mode since end Oct 2008 with many benefits:
Higher average brightness
Higher average current, constant flux
Improved stability
Constant heat load, beam current dependence of BPMs
Flexible operation
Smaller ID gaps, lower coupling
2008
2011
Top-up
Single-bunch top up application:
every 10 minutes with ~30-50 shots
current stability few 10-3
Injection efficiency 70-80% (~85% without IDs)
Ian Martin, ALBA Visit, Oct 2017

## Slide 10
Top-up
Four-kicker injection scheme
6 μs half-sine pulses
Stored beam kicked at least 3 times
Aligning current traces on scope produced poor injection efficiency
Best injection efficiency requires shift of kicker 2 timing (magenta)
Virtually impossible to match the pulses over the full train
1.87us
Ian Martin, ALBA Visit, Oct 2017
Stored beam
Injected beam
means 900/936 fill
Notes: 10
Wiggle is noise on pickups
K2 vessel resistance shows open

## Slide 11
Transient clearly visible by the beamline
Gating signals supplied to beamlines (not ideal)
Chop data measured during injection
Pause scan where possible
Re-normalise data where possible
Reduction of injection transient is an active area of study
Top-up
Kicker-01 vessel coating damage
10-15% intensity fluctuation
Trade-off between injection efficiency and stored beam oscillation
Kicker pulses not identical
  Best achieved:
  H: +/- 150 μm
  V: +/- 75 μm
Ian Martin, ALBA Visit, Oct 2017
courtesy C. McAuley, I03

## Slide 12
Bunch length
Intrinsic energy spread
(due to SR)
Synchrotron frequency
(osc. in long. plane)
Momentum compaction factor
(change in path length with energy)
Momentum compaction factor altered by changing the focussing strength of the quadrupoles.
Bunch length can be reduced from few×10 ps to few×1 ps in this way
4) Low Alpha: Special mode generating very short electron bunches. Storage ring is made quasi-isochronous
Low Alpha
Ian Martin, ALBA Visit, Oct 2017

## Slide 13
normal operation
“low-alpha” mode
15 mm
~15ps
~2ps
Bunch charge ~10μA
Low Alpha – Short Pulses
Ian Martin, ALBA Visit, Oct 2017

## Slide 14
Low Alpha – Coherent Emission
Low Alpha – Coherent Emission
Ian Martin, ALBA Visit, Oct 2017

## Slide 15
 | Short Pulse Mode | THz Mode
Momentum Compaction Factor | -1×10-5 | -4.5×10-6
Number of bunches | 400 + 1 | 200
Bunch current | 50 µA (93 pC) | 50 µA (93 pC)
Emittance coupling ratio | 0.3% | 1%
Lifetime | ~20h | ~20h
Injection efficiency (IDs open) | 30-40% | 15-20%
VRF | 3.4MV | 3.4MV
Micro-bunching instability threshold (SB) | ~30-35 µA | ~15 µA
Bursting threshold (SB) | ~55-60 µA | ~25-30 µA
The Diamond storage ring is run in a dedicated ‘low alpha’ mode 2-3 times per year Since Oct 2012, this has been in top-up with hourly injection cycles
Short pulse mode (NANOSCIENCE beamline I06):
Single bunch for time-resolved science
Electron bunch length reduced to ~3.5 ps
Priority on increased single bunch charge over minimum pulse duration (stable!)
THz mode (MIRIAM beamline B22):
Above bursting threshold to increase CSR gain in THz region
Priority to extend CSR spectrum towards 100cm-1
Low Alpha – User Modes
Ian Martin, ALBA Visit, Oct 2017

## Slide 16
α1 = -1x10-5
VRF = 1.5MV
Ibunch = 25µA
α1 = +1x10-5
VRF = 1.5MV
Ibunch = 25µA
Negative alpha operation benefits both short pulse and THz users:
  Bunch lengthening with current reduced
  ‘Sharper’ longitudinal profile
  Measured instability thresholds similar
α1 = +1x10-5 / 1.5MV
α1 = -1x10-5 / 1.5MV
Low Alpha
Ian Martin, ALBA Visit, Oct 2017

## Slide 17
03/10/2012
04/10/2012
05/10/2012
THz Optics (10 mA/200 bunches)
Short Pulse Optics (20 mA/400 bunches)
Nominal Optics
(250mA/686 bunches)
Low Alpha
Ian Martin, ALBA Visit, Oct 2017
courtesy G. Cinque

## Slide 18
Diamond Light Source
general introduction to the facility
different operating modes
top up, low alpha operation
Facility Upgrades / New Beamlines
increasing beam brightness
double mini-beta straight sections
exotic insertion devices
DDBA upgrade
Future developments
DIAD beamline
Diamond II?
Talk Outline
Ian Martin, ALBA Visit, Oct 2017

## Slide 19
Increases photon beam brightness:
Issues with components heating up, vacuum condition, RF trip reliability, ...
SC RF cavities now being supplemented by 2 EU HOM-damped NC RF cavities
Possibility to further increase beam current towards 500mA. Feasibility studies are under way - requires an additional RF cavity + HHC?
Top-up operation
Cavity 2B failure
Cavity 3C installed
Cavity 1A replaced by refurbished cavity 2B
Cavity 2B fails again, replaced with cavity 2D
Cavity 2D fails, replaced with cavity 1A
Beam Current
Ian Martin, ALBA Visit, Oct 2017

## Slide 20
In response to request from Science Division, emittance coupling has been reduced from 1% to 0.3% for user operation (27 pm.rad to 8 pm.rad)
Initially confined to machine development periods
Two week period from 17th October to 1st November 2012
Standard operational mode since 6th March 2013
Benefits include increased brightness / transverse coherence, smaller spot size
1% coupling
0.3% coupling
Reduced Vertical Emittance
Ian Martin, ALBA Visit, Oct 2017

## Slide 21
Reducing vertical emittance leads to small focus on sample
Reduced Vertical Emittance
Ian Martin, ALBA Visit, Oct 2017
courtesy K. Sawhney

## Slide 22
Reducing vertical emittance leads to higher spatial coherence
Reduced Vertical Emittance
Ian Martin, ALBA Visit, Oct 2017
courtesy K. Sawhney

## Slide 23
Introduced quadrupole doublets into long straights – reduces vertical beta function and allows 2 independent beam lines with in-vacuum IDs
Additional horizontal focussing allows the long beam line to have transverse coherent beam without losing flux
Double Mini-beta Optics
Ian Martin, ALBA Visit, Oct 2017

## Slide 24
Challenges:
new girders required
Strong instabilities (resistive wall)
Injection efficiency and lifetime degraded at some tune points
Double Mini-beta Optics
Ian Martin, ALBA Visit, Oct 2017

## Slide 25
Two APPLE-II IDs in single standard straight
Linear/circular/elliptically polarised light
Chicane magnets deflect electron beam at 10Hz
Allows beam line to rapidly switch polarisation
2 mrad photon beam separation
I10 (BLADE) Polarisation Switching
Ian Martin, ALBA Visit, Oct 2017

## Slide 26
I10 (BLADE) Polarisation Switching
Chicane deliberately ‘over-steered’ to produce flat-top profile
ID detuned to give similar intensity from upstream and downstream devices
Sample-point diode
Upstream intensity monitor
Ian Martin, ALBA Visit, Oct 2017
courtesy C. Bloomer

## Slide 27
For the ARPES beamline, a 5m long APPLE-II device was installed in Nov 2012:
Long straight section, beta functions larger than standard
Large tune-shifts in both planes that need to be compensated
Significant impact on the machine (reduction in dynamic aperture, lifetime)
Photon Energy | 18-240 eV
Device Period | 140 mm
Number of Periods | 34
Nominal Length | 4.995 m
Technology | APPLE-II
Minimum Gap | 23.5 mm
Peak Field | 0.9T (H) / 0.53T (C) / 0.63T (V)
Magnetic Material | NdFeB
I05 (ARPES) Beamline
Ian Martin, ALBA Visit, Oct 2017

## Slide 28
Dynamic multipole fields compensated using active shim wires (c.f. BESSY II)
Active shim wires
Insertion device
Residual kick
 |  | Tune Shift (ΔQx / ΔQy) | Beta Beat (x / y)
Vertical Polarisation | Uncorrected | -0.043 / 0.032 | 33% / 32%
 | Corrected | 0.003 / 0.003 | 3% / 3%
Circular Polarisation | Uncorrected | -0.030 / 0.026 | 22% / 23%
 | Corrected | 0.005 / 0.004 | 2% / 2%
Horizontal Polarization | Uncorrected | -0.003 / 0.015 | 2% / 13%
 | Corrected | 0.008 / 0.008 | 5% / 6%
I05 (ARPES) Beamline
Ian Martin, ALBA Visit, Oct 2017

## Slide 29
VMX Beamline
2 m U21 in-vac
0.7 m U30 ex-vac
Phase III micro/nanofocus MX beamline for atomic structure determination
Could be served by a short ex-vac undulator at the end of existing straight ….
…. but much better performance would be possible with a 2m long in-vac device!
Ian Martin, ALBA Visit, Oct 2017
courtesy E. Longhi

## Slide 30
New concept: Replace existing DBA cell with a modified 4BA cell (Double-DBA)
Introduces an additional straight section
Complete break of machine symmetry
Serves as a prototype for low emittance lattice upgrade
Lots of R&D required
DDBA cell
Additional straight
VMX Beamline: DDBA Cell
Ian Martin, ALBA Visit, Oct 2017
courtesy T. Pulampung

## Slide 31
Main Issues
Magnet Design (Danfysik):
  sector bend gradient dipole (0.8 T with 14 T/m)
  small bore quadrupoles (30 mm diameter, 70 T/m)
  high-gradient sextupoles (1600 T/m2)
Much reduced vacuum chamber in the arc (FMB)
octagonal 84×38 mm => elliptical 27×18 mm
Initial investigation of NEG coating chamber abandoned
too complex geometry for coating
systems of localised bumps to absorb radiation
Mix of stainless steel and copper
Engineering integration
standardisation of magnet lengths (one type of quads and sexts)
clashes between elements (space for coils overhang, flanges, …)
DDBA Cell Design Issues
Ian Martin, ALBA Visit, Oct 2017

## Slide 32
Preliminary AP lattice studies begun Jan 2013
Engineering design work started May 2013
External Review Committee approves design Nov 2013
Preparatory cabling work started Mar 2014
Magnets contract awarded to Danfysik Jun 2014
Vacuum pipe contract awarded to FMB Aug 2014
VMX optics frozen by end July 2014
Magnet delivery Jan 2016 onwards
First vacuum vessels delivered Feb 2016
Installation complete Nov 2016
Storage ring commissioned in 2 weeks Nov/Dec 2016
ID installed Mar 2017
First Light Apr 2017
DDBA Project Timeline
Ian Martin, ALBA Visit, Oct 2017

## Slide 33
DDBA Cell Installation
3 DBA girders replaced with 2 DDBA girders in a single 6 week shutdown
Ian Martin, ALBA Visit, Oct 2017

## Slide 34
Beam current = 300mA
(24/11/2016)
beam accumulation in the SR
(17/11/2016)
Beam current = 300mA
(24/11/2016)
DDBA Cell Commissioning
10 mA, initial orbit / optics correction on first day
Dipoles realigned to reduce correctors
All feedbacks / high-level software working
300 mA in 1 week
Vacuum conditioned in ~70 Ah
Ian Martin, ALBA Visit, Oct 2017
courtesy M. Cox
Notes: Loco tells us that the gradient is correct but the correctors tell us that the dipole is too weak – solution: move gradient dipole outwards

## Slide 35
beam accumulation in the SR
17/11/2016)
DDBA Cell Remaining Issues
Injection efficiency: ~85-90% => ~75-80%
Lifetime: 14.5 h => 13 h
Increase in vertical beam motion
Impact of SCW on emittance
Low alpha lattice
Ian Martin, ALBA Visit, Oct 2017
Notes: Loco tells us that the gradient is correct but the correctors tell us that the dipole is too weak – solution: move gradient dipole outwards

## Slide 36
Diamond Light Source
general introduction to the facility
different operating modes
top up, low alpha operation
Facility Upgrades / New Beamlines
increasing beam brightness
double mini-beta straight sections
exotic insertion devices
DDBA upgrade
Future developments
DIAD beamline
Diamond II?
Talk Outline
Ian Martin, ALBA Visit, Oct 2017

## Slide 37
Dual Imaging and Diffraction beamine
7-37 keV, 1 μm resolution
Several options investigated:
  Standard dipole source
  3T super-bend
  2nd DDBA cell?
Simulations for the second DDBA are showed further and significant degradation of dynamic aperture and especially lifetime
Decision taken not to proceed (for now)
An alternative proposal was put forward to remove one chromatic sextupole and insert a short miniwiggler (0.7 m) in its place
Simulations show this can work, local chromaticity correction deferred to the nearby sextupole
A project was launched in autumn 2016 for installation in 2018
DIAD Beamline
Ian Martin, ALBA Visit, Oct 2017

## Slide 38
DIAD
Missing sextupole compensated by doubling strength of partner
Permanent magnet wiggler 0.7 m placed in gap
V/H steerer, skew sextupole and BPM also removed
Lattice already tested with minimal impact on lifetime and injection efficiency
Girder construction underway
Due for installation first half of 2018
Ian Martin, ALBA Visit, Oct 2017
courtesy B. Singh

## Slide 39
Diamond operates since 2007 with nominal parameters
  (2.7 nm H emittance, 8pm V emittance, 300 mA)
However:
  2010 Petra-III was commissioned  1 nm H emittance
  2011-12 SLS and ASP ~1 pm V emittance (best achieved)
  2012 ESRF et al. operate with 8pm V emittance
  2013 ALS upgraded to a 2 nm H emittance lattice
  2014 NSLS-II started operation  0.5 nm H emittance
  2014 Petra III has tested a 160 pm lattice at 3GeV
  2016 MAX IV 300 pm H emittance lattice
  2018 SIRIUS 250 pm H emittance lattice
  2019 ESRF II 140 pm H emittance lattice
  APS, SPRING-8, ALS, BAPS, SLS, ELETTRA, SOLEIL, ANKA, ... are looking at lattice upgrades
Lattice Upgrade
Ian Martin, ALBA Visit, Oct 2017

## Slide 40
Lattice Upgrade
Theoretical Minimum Emittance (TME) achieved by shaping dispersion and beta-functions to have a waist in the centre of the bending magnets.
Practical techniques:
increase number of dipoles (MBA)
control Jx with trans. gradient dipoles
use long. gradient dipoles
reverse bending magnets
Reducing the emittance
Lowering the emittance is not the only goal: increasing the capacity for IDs also desirable
Ian Martin, ALBA Visit, Oct 2017
courtesy R. Bartolini
Notes: 40

## Slide 41
(Enabling a...) Stronger science case based on
higher brightness
higher transverse coherence
small photon beam size / divergence
cleaner spectral flux
Growing confidence (and first experience!) with MBA lattices
linear optics, nonlinear optics, instabilities
Growing confidence (and first experience!) with technolgical subsystems
magnets, vacuum, diagnostics, feedback
Lattice Upgrade
Hard X-ray CPMU
Soft X-rays APPLE-II
Transverse coherence fraction
120 pm.rad
300 mA
1 % coupling
Ian Martin, ALBA Visit, Oct 2017
courtesy R. Bartolini
Notes: 41

## Slide 42
Wish-list:
Emittance reduction to below 300 pm.rad (~100 pm.rad)
Reuse tunnel, beamlines and hardware (where possible)
Maintain mini-beta straight sections
Maintain short pulse capabilities (low alpha)
Phased installation (avoid long shutdown)
Minimise technology risks
Different options under study:
Initial studies of modified 4 Bend Achromat, (but also pure 5BA, 7BA, ...)
More beamlines vs. lower emittance
ESRF 7-bend HBMA Lattice => modified 6-bend HBMA solution
8-bend lattice? Reverse bends?
Lattice Upgrade
Ian Martin, ALBA Visit, Oct 2017

## Slide 43
Pros:
Magnet arrangement allows 24 additional short straight sections
Natural emittance 275 pm.rad (factor 10 reduction on present lattice)
Design utilises gradient bending magnets
Cons:
Emittance reduction judged too small
Difficult to achieve satisfactory lifetime and injection efficiency
3.35m
3.35m
Original DBA
4BA
Modified 4BA
Modified 4BA (DDBA)
Ian Martin, ALBA Visit, Oct 2017
courtesy T. Pulampong

## Slide 44
A more aggressive design proposed that merges the ESRF HMBA concept with the Diamond DDBA mid straight section taking the best of both
Use the ESRF cell (7BA with longitudinal gradient dipoles) – removing the mid dipole to make it a 6BA with a straight at the centre
Promising design:
Emittance 120 pm
~ 10mm DA
~ 3 h lifetime
short straight sections ~5m
long straight sections ~8 m
mid-straight section ~3 m
Control phase advance between dispersion bumps to cancel sextupole effects
6-bend HBMA (DTBA)
Ian Martin, ALBA Visit, Oct 2017
courtesy A. Alekou

## Slide 45
DTBA: Cell Optimisation
long straight
standard straight
new straight
Diamond II Super-Period
CELL 1
CELL 2
CELL 2
-CELL 1
Two kinds of cell used to reproduce the 6-fold structure of the present lattice (1 long and 3 standard straights per super-period)
Cell 1 is an asymmetric cell, +1.5 m longer than Cell 2
Dynamic aperture optimised by scanning linear optics parameters at fixed chromaticity
Ian Martin, ALBA Visit, Oct 2017

## Slide 46
Add additional quadrupole to increase beta-function at injection point
DTBA: Injection Cell
Dynamic aperture at injection point can be increased without affecting other cells
Momentum acceptance (lifetime) better without the cell …
courtesy A. Alekou
Ian Martin, ALBA Visit, Oct 2017

## Slide 47
DTBA: Open problems
I09/I13 vertical double mini-beta and horizontal focussing optics:
difficult to maintain in 8 m straight section
however these are “flagship beamlines” at Diamond
I13 is ~200 m long to an external building
Few other beamlines cannot be maintained:
I10 fast polarisation switching – does not fit in standard straight
I08 4.5 m ID is too long
I06 2×2.1 m APPLE-II plus phase units is too long
Bending magnet sources:
very likely they will be all replaced in the additional straight sections
B22 IR/THz radiation extraction from smaller pipe
Strong interest in maintain some kind of time-resolved capability
Ian Martin, ALBA Visit, Oct 2017

## Slide 48
Further lowering of the emittance?
courtesy P. Raimondi
Other options presently under study:
modified 8BA?
DQBA?
reverse bends, similar to SLS-II design?
accumulator ring for on-axis injection?
Ian Martin, ALBA Visit, Oct 2017

## Slide 49
Event | Date
Outline case approved by SAC and Board | April / June 2016
Board approves working on CDR and developing science case | Oct 2016
Internal / external science workshops | Mar-Sept 2018
Lattice frozen | Dec 2018
CDR ready | Mar 2019
Review of CDR (SAC, MAC, DISCo, etc) | Apr/May 2019
Board approves CDR and gives go-ahead for TDR and recruitment | Jun 2019
Draft TDR ready (including costs) | Mar 2020
Draft TDR reviewed by MAC and SAC | Apr/May 2020
Board approves seeking final approval | June 2020
Final TDR published | Sept 2020
Diamond II project approval | Dec 2020
Start calls for tender | Jan 2021
Start shutdown | Apr 2024
Resume full User operations | Oct 2025
Possible Timeline for Diamond II
Ian Martin, ALBA Visit, Oct 2017

## Slide 50
Diamond Light Source is a world-class facility for science:
Range of beam lines, each tailored to particular requirements of users
High brightness, stable, tuneable photons beams
Dedicate special modes (Short pulses, Coherent IR/THz radiation)
‘10-Year Plan’ aims to keep Diamond competitive:
Develop science case and technical design study for Diamond II
  Factor 10-20 × reduction of emittance, increased capacity for insertion devices
Reliability: RF improvement (solid state amplifiers, normal conducting cavities)
Photon Beam Stability (100Hz-1kHz), electron beam and photon beam at sample
Higher Current (>300mA), 3rd Harmonic Cavity + additional fundamental RF cavity
Undulator technology (CPMU / Superconducting Undulator)
Conclusions
Ian Martin, ALBA Visit, Oct 2017