## Slide 1
2D BPM Simulation Codes: BEM and FEM fusion
BpmLab (FEM) developed in ALBA in 2017, and BEM developed in Diamond in 2004, both made for Matlab, have been extensively used across synchrotron labs and accelerator machines for the last 10 years. These codes precisely meet the needs of the Accelerator community, offering rapid and precise simulations of BPM sensitivity function and other related effects. Other alternatives are not as straightforward or accessible (like the expensive codes CST, HFSS), or are much older and limited (as Poisson, GdFidl, etc.).
This work summarizes the capabilities and potential of these 2D codes: arbitrary geometry layout, wall current and sensitivity function calculation, 2D response maps and various non-linearity correction methods, showing the benefits of a possible fusion between both FEM and BEM
Andriy Nosych (ALBA Synchrotron)
Guenther Rehm (Helmholtz-Zentrum Berlin)
This presentation summarizes the capabilities and potentials of two well known 2D BPM simulation codes for Matlab: BPMLab and BEM, developed in the last 2 decades and extensively used across synchrotron labs and accelerator machines all over the world.
Currently these codes are still powerful but outdated, there is a lot of potential to update them, and moreover - combine them. We show the benefits of a possible fusion between both FEM and BEM. The work will take place during 2025, and the first united code is anticipated to be released for public in early 2026.
BPM Button Workshop. ALBA, Dec 12, 2024

## Slide 2
BEM (1D/2D)
also TodoGUI
for Matlab
All of them require external post-processing to access BPM-relevant parameters
Free
Fast
Flexible
Customizable
(Relatively) modern
All-in-one package
Community-made
Our current options to model and study BPMs:
BPMLab
Electrostatic FEM (2D)
for Matlab
Electrostatic (2D)
CST Studio ES ($$$)
Matlab PDE ($)
POISSON (old)
SuperFish (old)
Electro-magnetic (3D)
CST Studio Wake/PIC ($$$)
HFSS ($$$)
GdFidl ($, old)
Ace3P (complex)
Mafia (old)
BUT…
Not flexible enough!
OUTDATED!
Multitude of smaller-scale custom codes which exist in every lab

## Slide 3
ALBA
Soleil
ESRF
ILSF
CERN
ALS
Elettra
KEK
IHEP
BESSY
DESY
Sesame
CAS
INFN
Sirius
LNLS
HBNI
SLAC
DLS
KIT
…
2D finite element method-based (FEM) tool for Matlab that provides a fast and robust way to observe and treat the nonlinear distortion of a BPM.
Developed in 2016 in ALBA.
Later significantly extended under a collaboration with ESRF.
Used in a multitude of labs all over the world.
Contains an extensive editable real-life BPM library.

## Slide 4
Tool-box free, using open-source libraries:
Tetrahedral mesh generator DistMesh,
Fast Laplace 2D FEM solver with linear basis functions and boundary electric potential excitation (ref1, ref2),
Green’s reciprocity theorem used to get all beam positions in x4 simulations
Geometrical nonlinearity correction with linear scaling factors, 1D/2D polynomials (polyfitn) or direct voltage-to-position inversion (minFunc).
Main Features
OS/Matlab version-compatible (Win, Linux, Mac): tested for Matlabs v2013-2024
Arbitrary 2D geometry definition (analytic or polygonal): cross-sections of buttons, striplines, shoeboxes
Benchmarked VS. analytic wall-current method (WCM), BEM, CST (electrostatic, PS), ACE3P (T3P).

## Slide 5
WHY BPMLab?
2 or 4 electrode BPMs.
Intuitive geometry definition: combinations of several analytical shapes and polygons, most common to BPM designs.
A big library of real-life BPMs are directly available as editable presets.
Estimates linear region and calculate scaling factors.
Study and compare performance of chosen nonlinearity correction methods: with scaling factors, 1D/2D low/high power polynomials, and voltage-to-position inversion.
Geometrical imperfections studies: their effect on BPM response and electrical center.
Import of real BPM voltages for post-processing.
Signal manipulation studies: channel distortion, attenuation, amplification and their effects on response map.
SPS
EBS
Tesla
ELI
SESAME
LHC
Sirius
ESRF
LHC
EBS
ALBA
Petra3

## Slide 6
Linear correction by scaling factors:
2D Polynomial correction:
Voltage-to-position inversion:
BPM response map corrections within BPMLab

## Slide 7
Developed in 2004 in Diamond; later significantly extended with a GUI in ALBA in 2009.
Used across many labs, mainly customized versions.
Fast tool for Matlab with many useful calculations in one package.
BEM
Courtesy of G. Rehm, A. Olmos
Boundary element method (BEM) tool for Matlab that provides a yet faster way to calculate BPM sensitivity and other characteristics.
(and many more)

## Slide 8
MAIN FEATURES
OS/Matlab version-compatible (Win, Linux, Mac):
Tool-box free
BEM Solver: a simplified Electrostatic method to calculate wall charge from point charge excitation
Boundary contour discretization: few mesh nodes
Electrostatic problem dimension reduced to 1D: extremely fast calculation!
Courtesy of G. Rehm, A. Olmos
BEM is based on the PDE solution of the Poisson equation with Dirichlet boundary conditions.
Assuming flush electrodes, it has been reduced to deal with the boundary rather than the whole region, reducing the dimension of the problem to 1D.
BEM

## Slide 9
WHY BEM?
Point source excitation with a charge
Sensitivity calculation (DOS) for H and V axis
Power on electrodes for 50 Ohm load wrt. Beam current
Electrodes signal level wrt. Beam current
Capacitance calculation of electrodes
Intrinsic Resolution (Bw and temperature) vs. Beam current
BEM
Courtesy of G. Rehm, A. Olmos
Two scalable geometries available:

## Slide 10
BEM 1D
BpmLab 2D
2D volume mesh generator -> 10x thousands of mesh nodes.
Electrostatic potential distribution in closed volume.
Use of Greens theorem: 4x calculations of Poisson’s equation.
Electrodes are isolated from chamber.
Solver differences
BPM cross-section considered as closed contour.
1D Contour discretization -> Hundreds of mesh nodes.
Sections of contour considered as electrodes.
Wall charge is integrated over every section.
Electrodes are assumed flush with chamber.

## Slide 11
BEM
BpmLab
Old Matlab syntax < 2014 → slow code execution.
Use of java functions → slow code execution → Matlab to drop support of java soon.
Geometry optimization very complicated due to re-meshing at every step.
Graphics errors on different modern OS/machines.
Problems and disadvantages to date
Command-line version is the only maintained one
Few geometries available.
Most model and simulation parameters are hardcoded → not scalable.
GUI made for old versions of Matlab < 2009.
Every lab has their own edition.
Only bug-fixing makes sense.
Updates or extensions are complicated because of old code.

## Slide 12
COMBINING THESE TWO BRINGS A LOT OF POTENTIAL!
Speed
Flexibility
Scalability
Optimization
Machine Learning
In the future edition: new tabs!
Solver selection:
Electrostatics (FEM)
Boundary-element (BEM)
Electrode characteristics
Power, capacitance, intrinsic res., etc.
FEM
BEM
Education
Comparisons
Benchmark of two methods in one box
BEM works for hexagonal and round chambers with flush electrodes.
Hence, the only bottleneck could be complex geometries, e.g. striplines or asymmetrical chambers…
!

## Slide 13
For every button offset BpmLab needs a new 2D mesh: 10-30 minutes to make a good mesh.
Fresh example where a fast 1D solver would be more beneficial than 2D:
button misalignments study of ALBA-2 BPM [±10 um to ±2mm]
Min mesh edge: 15 um
Max mesh edge: 50 um
Mesh requirements for FEM:
This gif took >6 hours of compute. With FEM this would take minutes!
We discover that hor. electrical center position is quite linear and inv prop to button displacement.
retraction
protrusion

## Slide 14
A. Nosych, U. Iriso, J. Olle, "Electrostatic finite-element code to study geometrical nonlinear effects of BPMs in 2D", Proceedings of IBIC-2015, TUPB047 [PDF].
DIPAC07-MATLAB CODE FOR BPM BUTTON GEOMETRY COMPUTATION (Paper, A. Olmos)
Sensitivity calculation of beam position monitor using boundary element method, Tsumoru Shintake, Masaki Tejima, Hitoshi Ishii, Jun-ichi Kishiro. DOI: 10.1016/0168-9002(87)90496-7
http://www.lnf.infn.it/acceleratori/dafne/NOTEDAFNE/CD/CD-10.pdf DAPHNE TECHNICAL NOTE CD-10, "ANALYSIS OF THE DA?NE BEAM POSITION MONITOR WITH A BOUNDARY ELEMENT METHOD“, A. Stella
Ubaldo Iriso (ALBA), Marek Gasior & Manfred Wendt (CERN BI), Guenter Rehm (DLS), Kees-Bertus Scheidt (ESRF).
Special thanks to Jan Olle for his valuable contribution to the project at its birth.
Acknowledgements
References
Download and contact
BpmLab v1.24 (2024) Andriy Nosych (ALBA), anosych@cells.es
BEM/TodoGUI (2014) Guenther Rehm (Helmholtz-Zentrum Berlin), guenther.rehm@helmholtz-berlin.de
Slides and code: https://indico.cells.es/event/1542/

## Slide 15: Thank you for your attention!
ESRF, DEELS-2019
BEM
FEM

## Slide 16: extras

## Slide 17
Add noise (1%) to all channels: after DOS treatment
after Poly correction
ESRF SR: injection with RF off
Each dot:
position in one BPM (224 BPMs total)
Each image: turn
ALBA SR
Local bump, 4 orbit-correctors
Hor: 0 → 3 mm
Ver: 0 → 4 mm
Poly corrected
DOS
ESRF, DEELS-2019
Beam tests

## Slide 18
250 um
NOT OK
Examples of a badly converged mesh
OK
Properly converged mesh
Meshing:
Open-source tetrahedral mesh generator
based on metric functions (DistMesh).
Uniform or non-uniform meshes
User-defined min/max mesh size
Extremely reliable inner mesh
Boundary mesh QA: by eye. Always check!
FEM Solver:
2D electrostatic Poisson solver with linear basis functions and boundary electric potential excitation (Diriclet boundary conditions):
Green's reciprocity theorem: the surface charge induced on an electrode due to a test charge at (x,y) is proportional to the potential at that same position when the test charge is absent and the electrode is excited by a potential V.
4 calculations for all beam positions
ESRF, DEELS-2019

## Slide 19
How to correct?
Linear coefficient (real-time)
Polynomial families (real-time)
Specific formulae (real-time)
Lookup tables (post-process)
Voltage inversion (post-process)
ESRF, DEELS-2019
At what level? (by DS/Libera? by end-user?)
How fast? (TbT 100x kHz, FA 10x kHz, SA 10x Hz)
Perfect BPM & low noise stable electronics are still imperfect:
Linearity error

## Slide 20
2 polynomials need to be applied to each data sample:
A, B, C, D
ESRF, DEELS-2019
δx/Σ
δy/Σ
Px(δx/Σ, δy/Σ)
Py(δx/Σ, δy/Σ)
Polynomial correction seems to be the straight-forward solution if you want to have large beam drifts, and have fast real-time position nonlinearity suppression.
Polynomials are coupled 2D type.
Higher power = more coefficients, e.g.:
Max pwr 7: 36 terms
Max pwr 13: 105 terms
etc.