## Slide 1: Progress of the EIC HSR cold BPM mechanical design and integration
Workshop on button BPMs for synchrotron and light sources
Dec 11-12 2024
F. Micolon, D. Gassner, K. Matsushima and others
fmicolon@bnl.gov

## Slide 2: Introduction
The EIC will be the next collider to be built in the USA to probe the nucleon structure by shooting high-energy electrons (up to 18 GeV) on a high energy hadron nucleus (up to 275 GeV).
The hadron storage ring (HSR) is a reuse of the RHIC infrastructure (superconducting hadron collider) from the late-90s. The EIC beam parameters are not compatible with the RHIC stripline BPMs (designed for long hadron bunches)
The present talk will review some of the mechanical engineering challenges of the HSR BPM button design
We are looking for feedback from those who “have been there before”
Disclaimer
I am a humble mechanical engineer, not a BPM system expert
We are not a light source…but still a synchrotron !
Workshop on button BPMs
F.Micolon

## Slide 3: Outline
BPM system environment and requirements
Button design
Button and coax cable heating
Workshop on button BPMs
F.Micolon

## Slide 4: BPM system environment and requirements
Workshop on button BPMs
F.Micolon

## Slide 5: System requirement
Workshop on button BPMs
F.Micolon
The system is nested in a superconducting magnet environment and is at Lhe temperature (4 K)
A BPM is placed adjacent to each quad (every of betatron phase)
Electron-hadron synchronicity impose very large beam radial offsets compared to the aperture
Various operating mode with large bunch length variation (from 1500mm to 60mm)
Requirements
Requirement | Pilot bunch | Injection | Store
Max Bunch charge (nC) | 5 | 44 | 30.6
Beam current (mA) | 40 | 1000 | 690
Bunch length RMS (mm) | 1500 | 1500 | 60
Working range H (mm) | +/- 5 mm | +/- 5 mm | +/- 23 mm
% aperture | +/- 16 % | +/- 16 % | +/- 72 %
Resolution integrated 1s (mm rms) | 0.2 | 0.1 | 0.02

## Slide 6: System integration
Workshop on button BPMs
F.Micolon
Magnet vacuum vessel
Magnet helium vessel (cold mass)
Helium lines + superconducting bus
Quadrupole
Dipole
Beamline bellow
New BPM buttons
Decommissioned RHIC BPMs (striplines)
SiO2 signal cables
(in insulation vacuum)

## Slide 7: System integration
Workshop on button BPMs
F.Micolon
Magnet vacuum vessel
Magnet helium vessel (cold mass)
Helium lines + superconducting bus
Beamline bellow
New BPM buttons
Decommissioned RHIC BPMs
64 mm
48 mm
30°
Allowed beam excursion
At store
+/-23 mm
+/-2 mm
30°
Allowed beam excursion
At injection/ramp
+/-5 mm
The beam aperture has a “racetrack shape” through the superconducting magnets.
The beam excursion at store is a large proportion of the total aperture.
Challenging dynamic range for the button signal
Heating of the high side button and coax
The 30° corner button arrangement has been selected based on :
Overheating of the high side button if located in the horizontal plane
Integration of the rigid coax cabling

## Slide 8: Challenges of operating at large transverse offset
Workshop on button BPMs
F.Micolon
Planned operation at store
Large radial offset means operating in a very nonlinear regime.
The sensitivity drops from an estimated ~0.08 mm-1 to ~0.01 mm-1 at 20 mm offset.
Challenge to keep enough BPM resolution
Courtesy of Manfred Wendt
>0.01 mm-1
~0.08 mm-1

## Slide 9: BPM alignment strategy
Workshop on button BPMs
F.Micolon

## Slide 10: BPM alignment strategy
Workshop on button BPMs
F.Micolon
Requirement | Electrical center wrt quadrupole axis
Vertical (mm RMS) | 0.3
Horizontal (mm RMS) | 0.6
The RHIC quadrupole are powered in series with no shunt (expect a few quads)  No BBA possible
We don’t currently plan to wire scan the BPM aperture.
We plan to rely on BPM fiducialisation and Lambertson method to position the BPM electrical center to the quadrupole center (reference used for beam orbit control).
Alignment steps :
Step 1. BPM mechanical center-to-housing fiducialization
Step 2. Housing-to-cold mass coordinate system fiducialization
Step 3. Cold mass fiducials to quadrupole magnetic center
Step 4. Lambertson method to get the as-installed BPM electrical center offset
The following accuracy number are guesses - we will refine as we make our first alignment testing. We welcome your feedback !

## Slide 11: 1. BPM center-to-housing fiducialization
Workshop on button BPMs
F.Micolon
3x fiducial holder
(top and bottom)
We plan to use a 3D scanner to position the BPM mechanical center in the BPM fiducials coordinate system.
The datasheet accuracy of the 3D scanners we have been given is ~25-50 µm.
…But in our case the measurement will be done at an angle.
Estimated accuracy ~+/- 100 µm (?)
We plan to compare with a CMM measurement on a blank assembly (dummy buttons) to estimate the real accuracy.
If you have tried 3D scan before and have a feedback let us know !
1. Button face average plane
2. Project opposite button midplanes
3. Define center axis
(Intersection of midplanes)
4. Define BPM mechanical center
(intersection of axis and BPM centroid plane)
5. Reference BPM center in fiducials coordinate system

## Slide 12: BPM housing-to-magnet fiducialization
Workshop on button BPMs
F.Micolon
We will use a laser tracker to relate the BPM fiducials to the cold mass fiducials.
Estimated accuracy ~50 µm
The position of the quadrupole center has been measured for each SC quadrupole during construction.
Estimated accuracy ~ +/- 100 µm
We will use the Lambertson method to extract the electrical-to-mechanical center offset as-installed.
We have a wide bunch length variation from injection to store with varying frequency spectrum - can be a challenge for the Lambertson electrical center reference ?
Estimated accuracy ~ +/- 100 µm (?)
BPM module fiducials
Magnet cold mass fiducials

## Slide 13: BPM center-to-housing fiducialization
Workshop on button BPMs
F.Micolon
BPM module fiducials
Magnet cold mass fiducials
Tolerance stack-up | Tolerance
BPM mechanical center fiducialization (3D scan) | +/- 100 µm TBC
BPM housing-to-cold mass fiducialization (Laser tracker) | +/- 50 µm TBC
BPM cold mass-to quad center fiducialization | +/- 100 µm TBC
Electrical center offset determination (Lambertson) | +/- 100 µm TBC
Polynomial fitting error at high offset | TBD
BPM position distortion in operation | +/- 30 µm
SiO2 coax cable attenuation variation | TBD
Total tolerance RMS | < 300 µmTBC
Our approximate tolerance budget :
Looks like the budget can be help, but everything is still TBC pending a mockup of the whole alignment sequence and work on error estimation.

## Slide 14: BPM button design
Workshop on button BPMs
F.Micolon

## Slide 15: Button design
Workshop on button BPMs
F.Micolon
We have come up with a proposal button design that “fits the bill” but freedom is given to prospective vendor to propose variations depending on their fabrication techniques.
Conflat gasket
Stem (Inconel or 316L)
SiO2 insulator or Al2O3 (better for thermal)
RF spring seal
(trapped mode in annular gap)
Limited button radial clearance to avoid trapped mode
Solid copper button
Needs carbon coating for e- clouds
Stainless steel housing
RP SMA connector
ø18 mm
Ø51mm flange OD

## Slide 16: Button design
Workshop on button BPMs
Button face is recessed inside housing (between 0 and 0.1mm)
The button is laser welded or brazed to the stem
A tight radial gap is requested (0,5 mm to 0,25 mm)
And a good concentricity
Brazed Al2O3 or SiO2
F.Micolon
Venting hole (to insulation vacuum)
Planarity to be sure we can define 4x BPM planes that cross on a line

## Slide 17: Thermal aspects
Workshop on button BPMs
F.Micolon

## Slide 18: SiO2 cable heating
0.141” (ø3,6mm) SiO2 cable
0.090”
(ø2.29mm)
SiO2 cable
Workshop on button BPMs
F.Micolon
Heat conducted from RT
Cryostat feedthrough
T = 293 K
Heat shield intercept block
T = 50 - 80 K
Magnet line T = 4.5 K
RF signal attenuation heating
Beam resistive wall heating
+ electron cloud heating
SiO2 insulator
SiO2 cable
Approx length 1.5 m
Insulation vacuum (~10e-6 mbar)
Beamline vacuum (UHV)
Outside pressure

## Slide 19: Pickup heating
The button temperature is expected below 40 K in all cases.
This will be low enough to avoid significant H2 desorption.
Max allowable temperature = 40 K

## Slide 20
The 0.090” cable is more susceptible to attenuation variations (because higher dissipated power and less conduction).
However, in the signal voltage range expected, the attenuation is still stable for both cables.
Max expected peak voltage = 82 V
80K heat intercept
SiO2 cable heating

## Slide 21: Conclusion
Workshop on button BPMs
F.Micolon
We have done the “easy” part – defining what we want.
We have done the “less easy” part – keeping potential bidders in the loop to make sure someone is going to bid.
Now we need to do the “hard part” – negotiating with the vendors as they come up with what they can/cannot do
And the “harder part” – dealing with what gets delivered to us and its deviations to the plan
We also need to start prototyping the actual alignment sequence to make sure we haven’t been too optimistic…
For us, this workshop is an opportunity to get a feedback from the community and save time and costly mistakes.
So please raise any concern or reservation you may have with the plan or the design laid out !

## Slide 22: BPM module operational distortion
The interconnect below can pull transversely and displace the BPM module. This was reviewed.
60 N – max bellow sideway force’
Deflection = 16 µm
First vibration mode – 780 Hz

## Slide 23: Will the Additional Heat Load be Acceptable for the Cryogenic System ?
Heat going to the 4.5 K circuit for 4x cables:
Power (W) | RHIC | EIC – 0.141” cable | EIC – 0.090” cable
Heat to the 4.5K circuit | 0.22 W | 0.5 – 0.8 W | 0.1 – 0.35 W
The heat can be directed to the beam screen cooling circuit or the magnet cooling circuit.
Using the 0.141” cable :
For the magnet cooling lines, EIC cryogenics agreed that +10W between recoolers will be acceptable. This is 3.2 W.
For the new beamscreen cooling circuit, the design heat load is ~80 W (per 150m). The addition of BPM cooling is + 4%.
Using the 0.090” cable the heat generated would be about halved and almost identical to the RHIC status.
Regardless of the cable choice, the additional heat load is reasonable for the planned cryogenic circuits.
Charge #2, #5

## Slide 24: Will the Vacuum Chamber Temperature be Consistent with UHV Operation?
Desorption of gas from an aC coated surface vs temperature - Source : R. Salemme et al . Link
EIC vacuum agrees that at this stage, keeping beam wall temperature below 40 K will keep us clear of significant gas desorption (and associated vacuum degradation).
In all cases simulated, the beam chamber wall and BPM button temperature is below 43 K and can with simple measures be reduced below 40 K (strapping).
More analysis will be required but overall, the BPM module temperature is consistent with UHV operation.
Charge #2, #5

## Slide 25: Possible Coax Cryo-Cable Options
0.141” cable
0.090” cable
The plan is to use rigid coaxial cables with a low density SiO2 dielectric material.
The inner conductor will be bulk copper. The outer conductor will be a stainless-steel jacket with an inner copper coating.
Compared to the current RHIC BPM cables :
~3x bigger thermal conductivity for the 0.141” cable
~lower thermal conductivity for the 0.090” cable
RF attenuation is expected ~1.5x higher with the 0.090” cable.
The final choice of cable is pending the cost and the system performance study.
Sample cables
Low density SiO2 dielectric
RHIC today

## Slide 26: Tech Note Link
More details on the simulation and results can be found in the BNL technical note published earlier this year :
https://www.osti.gov/servlets/purl/1969913

## Slide 27: Copper Electrical Resistivity
Assumption for Cu conductivity
=5E+8
50K

## Slide 28: Impact on Vacuum
From V.Baglin lecture on cryopumping
Desorption of gas from an aC coated surface vs temperature - Source : R. Salemme et al . Link

## Slide 29: BPM Air Feedthrough Temperature
RHIC cold fill
A measurement campaign with thermocouples on the BPM feedthrough has started this year to validate the temperature of the warm end.
During the cold fill the feedthrough temperature has not evolved.