## Slide 1
Albert Van Eeckhout Alsinet
6 November 2024 – Postdoc Day
ALBA of the future:
ALBA today:
Application of optical metrology techniques

## Slide 2: The Scientific Background:
Educational Background:
  Ph.D. Thesis: Polarimetric methods for the image enhancement in biological applications ﻿ (advisors: Juan Campos and Angel Lizana)(Awarded with Premio Justiniano Casas)
  Postdoc stays: Ecole Polytechnique (Paris, 2021), ALBA synchrotron (Cerdanyola del Vallès, since February 2022)
Scientific Interest:
  Fields: Optics, Metrology, Instrumentation, Polarimetry
  Key achievements: First use of light depolarization anisotropy to enhance biological tissue imaging New stitching procedure for surface metrology (LEEP)
  Key publications: Synthesis and characterization of depolarizing samples based on the indices of polarimetric purity (2017) Polarimetric imaging of biological tissues based on the indices of polarimetric purity (2018) Depolarization metric spaces for biological tissues classification (2020) Polarimetric imaging microscopy for advanced inspection of vegetal tissues (2021)
  The stitching interferometry system of ALBA (2023)
Postdoc Day
6 November 2024
Notes: This should be 1 slide and take not more than 2 min.
Scientific interest: Please make sure that the three parts, field, key achievement, and publication should be coherent.
Field: typically 1 or maximal 2; point out the most important one in case that there are two
Key achievements: one or two; they should be easily described in a single phrase like: 1.) first measurement of XYZ; 2.) design of instrumentation to measure XYZ; organizing conference on XYZ
Key publications: if possible choose high impact publication and publications supporting your key achievements.

## Slide 3: Key Work from the Past:
Postdoc Day
6 November 2024
Indices of Polarimetric Purity (IPP)
P1, P2, and P3
x
y
Biological Sample
Depolarization
Global observables (commonly used):
Depolarization index (PΔ)
Depolarization power (Δ)
Measure the overall depolarization
But not the depolarization anisotropy
Measure the overall depolarization
and the depolarization anisotropy
Introduction in light depolarization:
Albert Van Eeckhout et al. Synthesis and characterization of depolarizing samples based on the indices of polarimetric purity, Opt. Lett. 42, 4155-4158 (2017).
Notes: This should take about 40% of the talk
Describe the scientific work you had done with
motivation why it is important
What exactly you have done and with whom
Are there any consequences from this work: you may have opened up a field, of there was a patent, any kind of IP……

## Slide 4: Key Work from the Past:
Epipremnum aureum (pothos) leaf measured at 530 nm
Depolarization in plant samples (microscopic scale):
Postdoc Day
6 November 2024
Intensity Image
Albert Van Eeckhout et al. Polarimetric imaging microscopy for advanced inspection of vegetal tissues, Sci Rep 11, 3913 (2021).
PΔ
P1
Depolarization images reveal raphides distributed over the leaf.
Depolarization anisotropy is now used for the early detection of plant diseases
Notes: This should take about 40% of the talk
Describe the scientific work you had done with
motivation why it is important
What exactly you have done and with whom
Are there any consequences from this work: you may have opened up a field, of there was a patent, any kind of IP……

## Slide 5: Goal for the ALBA Stay:
Motivation:
  Control high-precision instruments (with sub-nanometric resolution)
  Enhance my knowledge about optical metrology, x-ray optics and instrumentation
  Work in an interdisciplinary environment
  Meet new people from the synchrotron community for future collaborations
  Publish high impact articles
Long Term Goal:
  Consolidate and expand my knowledge in optics.
  Develop a scientific career as a scientist in the field of optical metrology.
Postdoc Day
6 November 2024
Notes: This will be the second 40%

## Slide 6
Optics Laboratory:
Improvement of the stitching interferometry system of ALBA for sub-nanometric surface metrology
Development of new techniques to measure strongly curved mirrors
Minerva Beamline:
Commissioning of Minerva
Bayesian orientation control system
Laser tracker positioning
Minerva Beamline:
Commissioning of Minerva
Bayesian orientation control system
Laser tracker positioning
Optics Laboratory:
Improvement of the stitching interferometry system of ALBA for sub-nanometric surface metrology
Development of new techniques to measure strongly curved mirrors
Work done at ALBA:
Postdoc Day
6 November 2024

## Slide 7
Surface under test (SUT)
Reference
Surface reconstruction
Previous work on stitching:
Linear Error Elimination Procedure (LEEP):
Postdoc Day
6 November 2024
(Curvature removed)
Zygo Calibration
nm
LEEP-xy (0.04 nm rms repeatability)
nm
Measured
  LEEP calibrates and removes all systematic additive errors, including the defects of the Reference
A. Van Eeckhout et al. SPIE proceeding (2023)

## Slide 8
Work on stitching:
Influence of measurement errors in stitching:
Postdoc Day
6 November 2024
  We have simulated the effect of several measurement errors in stitching (uncorrelated noise, turbulence noise, sub-aperture positioning,…).
  The main contribution of error comes from air turbulences.
  Propagation of turbulence increases with the length of the mirror.
  The turbulence noise of our lab was of 0.6 nm rms.
Contribution of 1 nm turbulence error on the SUT reconstruction
*stitching of 200 sub-apertures
Simulation

## Slide 9
Work on stitching:
Reduction of turbulence error:
Postdoc Day
6 November 2024
  Two approximations:
  Create an enclosure that reduces the fluctuations of the environment
  Create a controlled flux of zero mean high frequency air turbulences
  Fizeau interferometer heats the environment
A. Vivio et al. SPIE proceeding (2017)

## Slide 10
Work on stitching:
Reduction of turbulence error:
Postdoc Day
6 November 2024
  A reflective surface is measured 100 times with the fan on and off.
  Repeatability with the fan on is three times better.
  The mean of the measurements are the same (2.5 picometers of difference).
Repeatability Fan off (0.62 nm)
Repeatability Fan on (0.21 nm)
“Improving stitching interferometry measurements by a continuous air flow”, in preparation
Measured

## Slide 11
Work on stitching:
Reduction of turbulence error:
Postdoc Day
6 November 2024
  A 550 mm section of the old MSPD mirror is measured 10 times with our standard stitching procedure and with the fan on and off.
  Repeatability with the fan on is three times better.
Repeatability Fan off (0.46 nm)
Repeatability Fan on (0.15 nm)
“Improving stitching interferometry measurements by a continuous air flow”, in preparation
Measured

## Slide 12
Work on MINERVA:
MINERVA beamline description:
Postdoc Day
6 November 2024
  MINERVA is part of the NewATHENA mission.
  NewATHENA consist of building and launching an x-ray telescope build of 500 Mirror Modules.
  MINERVA role: align 4 stacks to produce a Mirror Module.
D. Heinis et al. SPIE proceeding (2024)

## Slide 13
Work on MINERVA:
MINERVA beamline description:
Postdoc Day
6 November 2024
  This beamline only has three optical elements:
    multilayer toroidal mirror
    mirror module
    detector
  The distance between the mirror module and the detector must be 12 ± 0.0001 meters, with a maximum error in the transversal direction of 50 μm.
  Constant orientation of the mirror module during the whole calibration. Maximum error of 1 arcsecond (4.8 μrad).
D. Heinis et al. SPIE proceeding (2024)

## Slide 14
Work on MINERVA:
Bayesian orientation control system:
Postdoc Day
6 November 2024
  Two autocollimators measure the orientation of the mirror with two reflective faces.
  The 3D orientation of the mirror is deduced from a Bayesian model.
  If the orientation of the mirror is deviated more than 0.5 arcsec, the hexapod corrects such orientation.
D. Heinis et al. SPIE proceeding (2024)

## Slide 15
Work on MINERVA:
Bayesian model measurement:
Postdoc Day
6 November 2024
H: 13 unknowns
D: 4 observations
Autocollimators measurements: , , ,
Forward problem (analytical solution)
D = g(H) =
H = g-1(D) =?
Inverse Problem
  We first measure 50 known orientations with the autocollimators (calibration data).
  New unknown orientations are calculated by combining the new autocollimators measurements with the calibration data.
  The Bayesian model gives the most probable result with a given uncertainty.
D. Heinis et al. SPIE proceeding (2024)
Measured

## Slide 16
Work on MINERVA:
Bayesian orientation correction:
Postdoc Day
6 November 2024
D. Heinis et al. SPIE proceeding (2024)
  Hexapod+mirror module block is moved with a vertical linear stage in a range of ±20 mm.
  Orientation with deviations higher than 0.5 arcseconds are corrected.
  Only 1 correction that takes from 1 to 2 seconds is needed.
Measured

## Slide 17
Postdoc Day
6 November 2024
  The work done in MINERVA made me meet colleagues from other areas
  I am in contact with colleagues from other Optical Laboratories of other Synchrotrons. For instance:
      Lei Huang (Brookhaven), Mourad Idir (Brookhaven)
      Amparo Vivo (ESRF), François Perrin (ESRF), Raymond Barret (ESRF)
      Simon Alcock (Diamond), Murilo Da Silva (Diamond)
      Other…
Networking:

## Slide 18
Postdoc Day
6 November 2024
Future work at ALBA:
Optics Laboratory:
  Development of new techniques to measure strongly curved mirrors
  Evaluating the existing stitching errors for strongly curved mirrors
  Beamline diagnostics (at-wavelength metrology)
  Learn beamline design
Beamlines:
  MINERVA laser tracker positioning
xp
Scanning direction
R(x)
Tp
U(x)

## Slide 19: Summary:
Postdoc Day
6 November 2024
Working at the Optics Laboratory
Learning a lot of optical metrology, x-ray optics, and instrumentation
My research is based on optical metrology topics (e.g. stitching interferometry systems)
I am collaborating with people from ALBA and other synchrotrons
Challenging topics to face with in the near future (e.g. curved optics)
Interested in developing a career in the field of optical metrology
Notes: 10% of the time
Try to summarize in a few bullet points; and try to be as precise in short as possible:
What are you good in; what you have already proven that you are good in? I am good
What is your goal for the ALBA stay.
What networks you have built during your stay at ALBA? I have met the people from the optical metrology laboratories of other synchrotrons.
Are there any issues which you have to overcome.

## Slide 20: Acknowledgements:
Postdoc Day
6 November 2024
Universitat Autonoma de Barcelona:
  Juan Campos
  Angel Lizana
Optics Laboratory Group:
  Dominique Heinis
  Igors Sicks
  Josep Nicolas*
  Guillem Alvarez (student)
Collaborators from other synchrotrons:
  Lei Huang (Brookhaven), Mourad Idir (Brookhaven)
  Amparo Vivo (ESRF), François Perrin (ESRF), Raymond Barret (ESRF)
  Simon Alcock (Diamond), Murilo Da Silva (Diamond)
Colleagues from ALBA
Notes: 10% of the time
Try to summarize in a few bullet points; and try to be as precise in short as possible:
What are you good in; what you have already proven that you are good in? I am good
What is your goal for the ALBA stay.
What networks you have built during your stay at ALBA? I have met the people from the optical metrology laboratories of other synchrotrons.
Are there any issues which you have to overcome.

## Slide 21: Thank you for your attention!
Postdoc Day
6 November 2024
Notes: 10% of the time
Try to summarize in a few bullet points; and try to be as precise in short as possible:
What are you good in; what you have already proven that you are good in? I am good
What is your goal for the ALBA stay.
What networks you have built during your stay at ALBA? I have met the people from the optical metrology laboratories of other synchrotrons.
Are there any issues which you have to overcome.

## Slide 22: Key Work from the Past:
Depolarization in animal samples:
Postdoc Day
6 November 2024
a1 = 3; a2 = 1, and a3 = 1
Intensity Image
Depolarization index (P∆)
Combination of IPPs
Dissected lamb heart measured at 625 nm
Albert Van Eeckhout et al. Polarimetric imaging of biological tissues based on the indices of polarimetric purity, J. Biophotonics 11(4), e201700189 (2018).
Notes: This should take about 40% of the talk
Describe the scientific work you had done with
motivation why it is important
What exactly you have done and with whom
Are there any consequences from this work: you may have opened up a field, of there was a patent, any kind of IP……

## Slide 23
Work on stitching:
Repeatability as a function of averaged files:
Postdoc Day
6 November 2024
D. Heinis et al. SPIE proceeding (2024)
(a)
(b)

## Slide 24
Work on stitching:
Why is the fan working?
Postdoc Day
6 November 2024
D. Heinis et al. SPIE proceeding (2024)
(a)
(b)

## Slide 25
Work on MINERVA:
Bayesian model:
Postdoc Day
6 November 2024
  We cannot model the Inverse problem.
  It forces a probabilistic approximation.
  Bayesian approach calculates the most probable result from the measurements with uncertainty (measurement errors).
D. Heinis et al. SPIE proceeding (2024)

## Slide 26
Work on MINERVA:
Bayesian orientation correction:
Postdoc Day
6 November 2024
D. Heinis et al. SPIE proceeding (2024)
  Mirror module is vertically moved with the hexapod in a range of ±20 mm.
  Orientation with deviations higher than 0.5 arcseconds are corrected.
  Only 1 correction that takes from 1 to 2 seconds is needed.
Measured
Autocollimator 1
Autocollimator 2
Correction
Correction