## Slide 1: RF plans for PETRA IV
ESLS RF & HarmonLIP Workshops 2025
Chris Christou on behalf of DESY-MHF
24th October 2025, ALBA Synchrotron

## Slide 2: Agenda
DESY site and accelerators
The PETRA IV upgrade
Project schedule
RF details and recent developments
Prototyping in PETRA III
Harmonic cavity options
Low level RF requirements
Stability issues and strategy

## Slide 3: The DESY accelerators
PETRA III
  6 GeV
  2304 m circumference
  120 mA current
  20 MV voltage
  LINAC II 450 MeV preinjector
  PIA accumulator
  DESY II booster
FLASH
  1.2 GeV
  315 m length
XFEL
  Up to 16.5 GeV
  3.4 km length
  200 m injector
  2 km linac
  1.2 km undulator/experiments

## Slide 4: Basic design and infrastructure overview
New extension hall PXW under public park
RF moves from South to new building in North
DESY injector complex upgrade
  New low-emittance booster
R Bartolini 9th General Low-Emittance Rings Workshop, 14th February 2024
1300 pm  20 pm

## Slide 5: PETRA IV parameters
Parameter | Brightness mode | Timing mode
Beam energy | 6 GeV | 
Beam current | 200 mA | 80 mA
Circumference | 2304 m | 
Revolution frequency | 130.121 kHz | 
RF frequency | 499.665 MHz | 
Harmonic number | 3840 | 
Bunch spacing | 4 ns | 96 ns
Number of bunches | 1920 | 80
Energy loss per turn | 4.2 MeV | 
RF voltage | 8 MV | 

## Slide 6: PETRA IV project schedule
2025 | FLASH upgrade and XFEL Long Installation and Maintenance Period Installation of new XFEL gun PETRA IV Preparation Project ongoing Design and manufacture of third harmonic cavity and suitable amplifier Publication of Engineering Design Report
2026 | PIA renovation PETRA IV approval expected End of Preparation Project
2027 | Procurement begins
2028 | 
2029 | End of PETRA III operation
2030 | 2.5 year dark- time begins
2031 | 
2032 | PETRA IV starts operation

## Slide 7: RF parameters
 | Fundamental RF | Harmonic RF
RF frequency | 499.665 MHz | 1498.995 MHz (third harmonic)
RF voltage | 8 MV | 2.2 MV
Number of cavities | 24 | 24
Shunt impedance per cavity | 3.4 MΩ | 1.5 MΩ
Unloaded quality factor | 29000 | 17000
Cavity coupling factor | 3.3 (critical) | 3 (overcoupled)
Total forward power to cavity | 1340 kW | 71 kW
Total reverse power | 0 kW | 34 kW
Power per RF station | 56 kW plus losses | 3 kW plus losses
Number of cavities follows analysis of capital and running costs
  Use EU/HOM damped cavities for fundamental system
Third harmonic cavity parameters satisfy flat bunch parameters
  Baseline design uses Alba scaled HOM-damped cavity

## Slide 8: DESY IV booster and options
Parameter | Value
Circumference | 304.8 m
Harmonic number | 508
Injection energy | 450 MeV
Extraction energy | 6 GeV
Repetition rate | 5 Hz
Energy loss per turn | 6.67 MeV (at extraction)
RF voltage | 10 MV
Cavity type | 5-cell HERA
Shunt impedance | 15 MΩ
Number of cavities | 9 (8 active)
Power per cavity | 62 kW
Use 9 * 5-cell cavities
  8 operational cavities and one standby
  HERA cavities can be reused
  Each cavity is powered independently by solid-state amplifier
Lattice has 8-fold symmetry
Distribute cavities around ring
  8 cavities in pairs in 4 straights
  9th cavity installed in own straight
  Alternatives are under consideration
  Retain DESY II
  Emittance high for injection into PETRA IV
  Laser plasma injector
  Initial results are promising
  Test injection into DESY II in 2026

## Slide 9: Reduction of installed RF capacity in PETRA IV
Cavities in groups of 4
  Vector sum control compensates cavity loss
  Three cavities must compensate loss
Independent cavity control
  Fast reaction not necessary
  23 cavities available to correct voltage
  Significant reduction of installed RF capacity
  ELEGANT simulation
  S. Antipov
  Beam survives cavity loss

## Slide 10: PETRA IV prototype in PETRA III
Single EU HOM-damped cavity has been in PETRA III ring since January 2023
  Passive conditioning with beam until July 2023
  120 kW solid-state amplifier installed in July 2023
  Routinely operated up to 400 kV and to 50 kW
  Using DESY MicroTCA-based LLRF
  No major problems have been encountered

## Slide 11: Layout of RF straight and RF hall
RF straight will be relocated to ring North
  Tunnel is above ground All cavities in single RF straight with new RF hall built alongside
  Hall houses transmitters, cooling infrastructure, power supplies, LLRF…
  Cavities grouped to minimise number of beam-tube tapers arising from cavity inner diameter differences
RF straight infrastructure requirements
Total wall-plug power for RF: 2.8 MW
Total cooling water flow for RF: 216 m3/hr

## Slide 12: Harmonic cavity options
Cavity Parameter | Scaled HOM Damped Cavity | Choke Mode Cavity
Shunt Impedance RS | 1.1 MΩ | 1.6 MΩ
Unloaded Quality Factor Q0 | 14000 | 19000
Coupling Factor | Fixed at installation: 3.5 | Variable from 0.1 to 5
Baseline
  Scaled HOM-damped cavity
  Proven at BESSY
Option
  Choke mode cavity
  In production
  Manufacturing complete in 2026
  Test and decision in 2027

## Slide 13: Choke-mode cavity
The TM010 mode is rejected by the choke. Due to the distance of l/2 between the short circuit of the choke and the annular output of the cavity, the TM010 mode "sees" a short circuit
Tsumoru Shintake: “The Choke Mode Cavity”, 1992 Jpn. J. Appl. Phys. 31 L1567
T. Inagaki et al.: “High-gradient C-band linac for a compact x-ray free-electron laser facility”, PRSTAB, 17, 080702 (2014)
Silicon carbide absorber rings are fixed in position with a titanium spring

## Slide 14: DESY “Shintake” choke mode harmonic cavity variant
Single cell design
Adjustable coupler and tuner
 | Arguments
Advantages | The HOM damper capabilities are not frequency limited
 | Mechanical construction is simple
 | Only a small number of cooling circuits required
 | High power coupling factor can be varied from 0 to 5
Disadvantages | Frequency of the cavity body and the choke must be precisely matched to each other
Cavity construction status
  Design is complete
  Manufacturing drawings have been produced
  First components have been delivered
  Construction complete in late 2026
  Test in 2026/27

## Slide 15: Analytic estimation of power dissipated in HOM-loads
Parameters of the 500MHz HOM Damped Cavity | 
Gap width g | 226 mm
Beam pipe radius a | 37 mm
Shunt impedance RS | 3.4 MΩ
Unloaded quality factor Q0 | 29910
Frequency fRF | 499.665 MHz
Parameters of PETRA III | 
Circumference of PETRA III | 2304 m
Revolution time T0 | 7,69 ms
Number of circulating bunches Nb | 40 (timing mode)
Electron beam current | 100 mA
Longitudinal bunch length sl | 13,2 mm
Each HOM-damper of the cavity has to dissipate 342 W during the PETRA III timing mode
Power loss in all Modes:
Power loss into the fundamental mode only:
Power loss into the HOM damper:
Application of the analytical approach of R. B. Palmer (1989)

## Slide 16: Measurement of HOM-load in PETRA III
The measurement and analytical calculation are remarkably close to each other:
Energy loss into HOM`s calculate by theory: 1025W
Measurement has delivered: 955 W
Measurement of the HOM power loss by observing the temperature of the cooling water temperature leaving the ferrite HOM dampers
Beam current was decreased from 100 mA to 29 mA within 2.8 h which keeps the HOM dampers in an equilibrium at all beam currents.
Constant gap voltage keeps the heat contribution due to heat conduction from the fundamental mode in the HOM damper constant.
Observation: The HOM load is different for all three HOM dampers.
The arrangement of the tuner and coupler forces the dipole HOM modes to polarize into an upright position.
This means that the HOM load is highest for the upright HOM damper waveguide.
40 bunches, beam current decreases slowly from 100 mA to 29 mA

## Slide 17: Low-level RF: design and tolerances
MicroTCA-based digital LLRF
  Development of XFEL system applicable to CW operation
  Four cavities controlled independently per µTCA crate
  LLRF controls Beckhoff PLC plunger driver
  Required tolerances 10 x looser than XFEL values
    0.1% rms amplitude stability
    0.1° rms phase stability
  Prototype has been running successfully in PETRA III since 2023

## Slide 18: Stability issues with harmonic cavities
Very high coupled bunch mode driving impedances
  Low rotation frequency and broad cavity impedance combine to destabilise beam
  There are many problematic modes
  Initial analytic estimates are confirmed by ELEGANT simulation (Y-C Chae & C Li)
Flat potential
Detuned

## Slide 19: Instability control with direct RF feedback and one-turn delay
Reduce driving impedance with direct RF feedback
  Successfully implemented at CERN and PEP II (Pederson 1975, Minty 1996)
  Previously used in HERA at DESY with amplifier in tunnel (Gamp 2011)
  Requires development of sophisticated comb filter in one-turn delay line (Mastoridis 2012 )

## Slide 20: Initial tests of direct RF feedback
Proof of principle measurements on test cavity and HOM-damped cavity
  Impedance (and HPA gain) change with feedback gain (attenuation)
  Feedback gain calculated from S21 measurements
  Also from Fano profile of S11 and S22
Feedback loop stability
  Quantified by gain and phase margin
  Consistent with theory

## Slide 21: Parking the harmonic cavities
 | Number of cavities | R0 | Q0 | Coupling factor | Tuning range
Choke-mode (Shintake) cavity | 24 | 1.7 MΩ (design) 170 kΩ (design, shorted) | 19300 (design) 2010 (design, shorted) | Variable, can be disabled by shorting the input coupler | 3 MHz, with shorted frequency 3 MHz above active frequency
Alba cavity | 24 | 1.5 MΩ (design) 1.05 MΩ (measured) | 17000 (design) 13200 (measured) | Fixed (nominally β = 4) | 12 MHz
Summed impedance of 24 harmonic cavities breaches the longitudinal instability threshold
  Detuning and differential tuning reduces the effect
  Limited tuning range of Shintake cavity leads to more pronounced effects

## Slide 22: Summary
PETRA IV upgrade is an ambitious programme involving new storage ring and booster plus considerable civil development
Hoping for funding approval in 2026 and a 2½ dark period for upgrade beginning in 2030
RF design is largely fixed
Fundamental cavity, solid state amplifier and digital LLRF have been tested in PETRA III
Baseline harmonic cavity is ALBA active 3rd harmonic design and “Shintake” choke mode cavity is being developed as an alternative
Stability is a considerable challenge and will be addressed by feedback impedance control
Thank you for your attention
Any questions?