## Slide 1
ALBA labs
Magnetic lab
RF lab
Vacuum lab
Francis Perez

## Slide 2
Magnetic Measurements Laboratory
Belongs to ALBA accelerators division
Specialized in accurate measurements of big magnetic structures

## Slide 3
Magnetic Measurements Laboratory

## Slide 4
Measurement benches
  Hall probe bench
    Partially build in-house
  Rotating coil bench
    Purchased from CERN
  Flipping coil bench
    Purchased from ESRF
  Fixed stretched wire
    Designed and built in-house
  Helmholtz coils
    Purchased from Elettra
Magnetic Measurements Laboratory

## Slide 5
  Hall probe bench
  Rotating coil bench
  Flipping coil bench
  Helmholtz coils
  Fixed stretched wire bench
Magnetic Measurements Laboratory

## Slide 6
In order to build the accelerators, ALBA did set up a complete magnetic measurements laboratory specialized in characterization of big magnetic structures used in accelerators physics and technology
Magnetic measurement capabilities
    Bx, By, Bz bench (Hall)
    Iz bench (Rotating coil)
    Mx, My, Mz (Helmholtz)
    Ix, Iz (Stretched wire / flipping coil)
Magnetic Measurements Laboratory

## Slide 7
Magnetic Measurements Laboratory

## Slide 8
Mission of the laboratory:
Measurement of Storage Ring Magnets
  Measurement of magnetic field maps
    Hall probe bench
  Measurement of multipoles
    Rotating coil bench
Construction and measurement of IDs
  Permanent magnet blocks characterisation
    Helmholtz coils & Fixed Stretched wire
  Measurenent of magnetic field maps
    Hall probe bench
  Measurement of field integrals
    Flipping coil bench
Magnetic Measurements Laboratory

## Slide 9
SESAME dipoles (2014)
CIEMAT magnets for IFMIF
Magnets for ESRF upgrade
CIEMAT phase shifter for E-XFEL
Collaboration with other research centers
Magnetic Measurements Laboratory

## Slide 10
High Power RF Laboratory
Belongs to ALBA accelerators division
Specialized in low and high RF power measurements and cavity conditioning

## Slide 11
In order to build the accelerators, ALBA did set up a complete high power RF laboratory for prototype testing and cavity conditioning.
Bunker 4.1 x 3.4 m2
High Voltage Power Supply 38 kV – 4 A
IOT amplifier 80 kW – 500 MHz
Waveguide system WR1800
LLRF Digital IQ
Controls Tango
High Power RF Laboratory

## Slide 12
High Power RF Laboratory

## Slide 13
  Cavity inside the Bunker
  Waveguide System
  LLRF and Controls racks
  RF transmitter
High Power RF Laboratory
  IOT cabinet
  HVPS

## Slide 14
High Power RF Laboratory
RF lab

## Slide 15
Mission of the laboratory:
LLRF tests
Amplifier IOTs test
High power RF conditioning of:
  Cavities
  Input power couplers
High Power RF Laboratory

## Slide 16
Collaboration with other research centers
CIEMAT
IFMIF
Buncher cavity
(2014)
CIEMAT - Cyclotron Cavity (2014)
High Power RF Laboratory

## Slide 17
Vacuum Laboratory
Belongs to ALBA Engineering division
Specialized in Ultra High Vacuum: design, construction and tests.
Staff:
2 vacuum engineers
2 Vacuum technicians

## Slide 18
Vacuum Laboratory

## Slide 19
Installation and Material :
Clean room class 100000 (ISO 8)
Bake out oven (length 14m,height 1m,width 2m)
12 roughing station
7 leak detectors
Material for bake out (controllers, heaters …)
Ion pumps
Residual gas analyser
Vacuum measurement gauges
Traveling crane (1T)
Design and Calculation
Nx (Siemens) Cad system
Ansys for calculation
Molflow for vacuum calculation
Vacuum Laboratory

## Slide 20
ALBA VACUUM SYSTEM
Based on lumped Absorber
16 Cells:
8 Unit Cells ~12,5m
8 Matching Cells ~10,3m
4 Long straight sections 8m
12 Medium straight sections 4m
8 Short straight sections 2m
Complete Cell baked out in a special oven
no bake out in situ except straight sections
3 Aluminium Neg coated chambers (medium straight)
2 In vacuum ondulators (medium straight)
Vacuum Laboratory

## Slide 21
MAXLAB (Sweden):
Design of vacuum chambers for the 3Gev and 1,5Gev MaxIV Storage Rings
Thermal, mechanical and vacuum calculation
Technical specifications & CFT process
Design review meeting with vacuum experts (CERN,BNL,GSI,SOLEIL)
Meeting with CERN for coating collaboration
Salamanca University (Spain)
Design and calculation of a vacuum chamber for a 200TW laser compressor optical devices
Technical specifications & CFT process
Fabrication follow-up
Installation and vacuum tests
Vacuum Laboratory
Collaboration with other research centers

## Slide 22
Conclusion
Three labs, developed for the construction of ALBA:
  Magnetic Lab
  RF lab
  Vacuum lab
are now ready and used for:
  ALBA upgrades
  Collaborations
Thank you