## Slide 1
MACHINE OPERATION AT ALBA
Montse Pont, CELLS-ALBA
16-18/12/2013

## Slide 2: Outlook
Introduction to ALBA accelerators
Operation of ALBA accelerators in 2013
Ongoing projects

## Slide 3
ALBA Accelerators
LINAC
100 Mev
BOOSTER
100 MeV – 3 GeV
STORAGE RING
3 GeV

## Slide 4
100 MeV LINAC
Main LINAC parameters
Turn-key system
Single and multibunch operation
Repetition rate up to 5 Hz

## Slide 5
Multibunch mode
4 nC at linac exit
Main linac parameters:
Few bunches mode
0.25 nC/bunch at linac exit
ex (norm.) ≈ 9 mm·mrad
DE/E = 0.16% (rms)
100 MeV LINAC

## Slide 6
Main BO parameters:
C = 249.6 m, shares tunnel with SR
E = 110 MeV to 3.0 GeV
ex ≈ 9 nm·mrad
Repetition rate: 3.125 Hz
Lattice: 4 x fold symmetry
Orbit correction:
    28 BPMs
    44 HOR_CORR + 28 VER_CORR
    9 are ramped, 63 @ dc
BOOSTER

## Slide 7
3 GeV
200 MeV
BOOSTER
BO matching cell

## Slide 8
STORAGE RING
Electron beam energy 3.0 GeV
Storage Ring Circumference 268.8 m
Number of cells 16
Symmetry 4
Straight section lengths 4 x 7.8 m ( 3 ID’s)
12 x 4.3 m (12 ID’s)
8 x 2.3 m ( 1 ID’s)
Beam current, nominal 250 mA
Emittance 4.3 nm.rad
Tunes 18.18, 8.37
RF frequency 500 MHz
Coupling 0.6 %
Lifetime @ 125 mA 22 h
Main parameters of the Storage Ring

## Slide 9
σx = 132 μm
σ’x = 46 μrad
σy = 7.5 μm
σ’y = 5.8 μrad
σx = 270 μm
σ’x = 20 μrad
σy = 16 μm
σ’y = 2.7 μrad
σx = 310 μm
σ’x = 22 μrad
σy = 15 μm
σ’y = 2.9 μrad
long
medium
medium
short
STORAGE RING

## Slide 10
SOFB
Running every 3 s
With RF frequency included on SOFB
RMS-Values:
σx = 0.5 μm
σy = 0.2 μm
Beam Stability over 24 h
CLOSED ORBIT

## Slide 11
FE (source) | Source distance | eBPM data |  | XBPM data | 
 |  | Horizontal | Vertical | Horizontal | Vertical
FE09 (bending) | 7.00 m | ----- | 0.5 μm | ----- | 2.5 μm
FE04 (SCW31) | 8.66 m | 1.5 μm | 0.8 μm | 3.0 μm | 1.0 μm
FE11 (IVU21) | 10.29 m | 1.2 μm | 0.9 μm | 3.0 μm (fixed gap) | 1.5 μm (fixed gap)
FE13 (IVU21) | 9.85 m | 1.2 μm | 0.9 μm | 3.0 μm (fixed gap) 10 μm (moving gap) | 1.5 μm (fixed gap) 5 μm (moving gap)
Photon beam stability @ FE13-XALOC on 2012/03/24 (fixed gap):
vertical plane
horizontal plane
Projection
eBPMs
FE XBPM
rms photon beam stability for different FEs

## Slide 12
projection eBPMs
(BPM05_2 & BPM05_3)
FE09 XBPM
SR current
2012/07/18 @10:00 new SOFB (elog 726)
Introduction of xbpm on SOFB for BM BL

## Slide 13
Phase I beamlines: 6 x IDs
1 x Bending
Spectral range: from UV (80 eV) to hard x-rays (50 keV)
High brilliance: 1020 at 2 keV
STORAGE RING

## Slide 14
CLOSING THE IDs: Horizontal orbit deviation
± 10 um
MPW
Apple-II
Apple-II
IVU
SCW
Additional correction coils installed
ID COMMISSIONING

## Slide 15
± 10 um
MPW
Apple-II
Apple-II
IVU
SCW
CLOSING THE IDs: Vertical orbit deviation
ID COMMISSIONING

## Slide 16
IVU21
MPW80
TUNE SHIFT
ID COMMISSIONING

## Slide 17
OPERATION 2013
  Scheduled for 2013: 5280 h of operation
  3555 h for BLs (excluding injection)
  1488 h for AD & radiation tests

## Slide 18
OPERATION 2013
Chart: hours [h]
schedule initial | 450 | 472.5 | 337.5 | 337.5 | 337.5 | 472.5 | 360 | 472.5 | 315
schedule revised | 448 | 470.5 | 0 | 0 | 0 | 649.5 | 492 | 493 | 515.5
delivered | 441.36 | 459.85 | 0 | 0 | 0 | 609.95 | 483.28 | 469.3 | 508.33
Beamline operation: 3555 h Scheduled January
  4081 h Re-scheduled July
  2972 h Delivered
  84.0 % Beam availability (over initial schedule)
Cooling unstable hydraulically

## Slide 19
Down time (1109 h) per sub-system
91 % due to the unstable cooling
OPERATION 2013

## Slide 20
Down time (97 h) per sub-system
(w/o cooling & exchange of vacuum chamber considered)
OPERATION 2013

## Slide 21
MTBF = 24.75 h
OPERATION 2013
Accelerator Availability: 97.0 %

## Slide 22
Running 3 shifts/day
Runs of 24 days on average
2 long shut downs, 7 short (1 w) shut downs
Monday: Accelerators start-up
Tuesday 07h00 – Monday 07h00 Beam for users
ALBA OPERATION

## Slide 23
  CR manned 24 h when beam in the machine
  Always 2 people on the CR
  Crew of operators to guarantee operation
  People on shift: dedicated OP + a member of the Accelerator Division
  CR also manned during shut downs: 1 OP/day (8h)
ALBA OPERATION

## Slide 24
  First tests of top-up over 6 h
TOP-UP

## Slide 25
Beam line safe for top-up if (I.Martin, Diamond):
Electrons travelling forwards from straight section cannot pass down beam-line
Electrons travelling backwards from beam-line cannot pass through to straight section
Electrons travelling in either direction do not have same trajectory at any intermediate point

## Slide 27
  PSS upgrade
    Energy matching between BO and SR:
    BT_BEND_02 within +/-5 A of the nominal setting
    Disables Linac and BO-RF
     Additional hardware intlk: installed and tested
    Warning level on any radiation monitor (accumulated dose > 1.5 uSv)
    Disables Linac and BO-RF, decay mode for max 4 h.
    Stored beam < 20 mA
    Closed FEs
    Alarm level on any radiation monitor (accumulated dose > 2.0 uSv)
    Kills beam and closed FEs

## Slide 28
    No bucket selection: Multibunch injection
    Re-use existing injection DS & GUI
    Additional conditions for top-up:
    min. lifetime: 10 h
    min. injection efficiency
      to avoid injecting with a low injection efficiency, number of shots will be limited
    Project started for single bunch injection with bucket selection using a time correlated single photon counter

## Slide 29
    Jan - April further tests:
      BLs tests
      Radiation measurements
      GUI debugging
  Di = 1 mA, injections every 10 min

## Slide 30
Scheme
88 BPMs: [x,y] data at 10 kHz
88 H Correctors
88 V Correctors
Data transfer
Correction computation
Write in 176 PS
FOFB

## Slide 31
  Tests w/o beam
  Tested electronics latency
  Measured latency of 380 us

## Slide 32
  Latency of the whole system
      Including iron core corrector coils
      Including vacuum chamber
        Tests with beam ongoing
DAC PS output
Sniffer detection of change
1.8 ms
Measured latency of ≈ 1-2 ms
Ok. with previous simulation
Ok. for 100 Hz correction

## Slide 33
Accelerators operate reliable for users
    97% 2013
Objectives for 2014
  FOFB
  Top-up
  Injectors stability
  Bunch by bunch feedback
  Increase operation current
May 2014
End 2014
On going
SUMMARY