## Slide 1
ALBA RF Systems
Francis Perez

## Slide 2
ALBA Accelerators
LINAC
100 Mev
BOOSTER
100 MeV – 3 GeV
STORAGE RING
3 GeV

## Slide 3
LINAC RF System

## Slide 4
Electron Gun : Thermionic (Pierce type), 90 kV DC gun with grid modulator at 500 MHz
Bunching Section: Pre-buncher: single cell @ 500MHz
Buncher: 1 SW bunching section @ 3GHz
Energy at the bunching section output = 16 MeV
2 Acc. sections: TW 2/3π Constant Gradient 3 GHz.
Energy gain= 55 MeV @ 20MW nominal input power.
2 Klystron modulators: 35 MW each klystron at 3GHz.
The first one feeds the 3 GHz bunching section and the 1st acc. structure.
The second one feeds the second accelerating structure
Linac RF
Thales Turn Key
100 MeV

## Slide 5
Klystrons: 3 GHz - 35 MW - pulsed
Linac RF
Modulators: 270 kV – 290 A
PS
Vacuum
Controls

## Slide 6
Linac RF
 | P [MW] | E [MeV]
Buncher | 5 (K1) | 15
Acc.section 1 | 20 (K1) | 55
Acc.section 2 | 20 (K2) | 55
EXIT | 45 MW | 125 MeV

## Slide 7
Booster RF System

## Slide 8
Booster RF
At 3 GeV:
RF Voltage 1000 kV
Beam current 4 mA
Losses 627 keV/turn
Beam power 2.5 kW
Cavity power 34.5 kW
TRANSMITTER
Tube type IOT
HVPS 36 kV / 4 A
RF Power 80 kW
Efficiency > 60%

## Slide 9
Booster RF
Cavity: 5 cell Petra type
Basic Parameters
    Rshunt 15.4 MW
    Maximum Power 75 kW
    Length 1,65 m

## Slide 10
Storage Ring RF System

## Slide 11: Power Requirements
Beam current 400 mA
Bending losses 1000 keV/turn
ID losses 300 keV/turn
Other losses 50 keV/turn
Total losses 1350 keV/turn
Beam power 540 kW
Energy Acceptance 3 %
SR RF

## Slide 12
Layout 6 cavities
Digital
LLRF
RF Voltage 3600 kV
TRANSMITTER
Tube type IOT
Number 6 x 2 IOTs
Power 2 x 80 kW
Combination CaCo
SR RF

## Slide 13
Transmitter (Thomson)
HVPS Cabinet:
36 kV – 4 A power supply
60 Pulse Step Modulation Cards
New PSM card 700V – 4A
SR RF
HVPS
IOT Cabinet
IOT Cabinet:
80 kW IOT
400 W SSA
Auxiliaries
Controls PLC

## Slide 14
6.8 MHz
Improvements
LS-IOT (Light Source IOT in collaboration with Thales)
New cavities with 6 1/8’ coaxial output
Tube with wider ceramics
Tested in factory at 80 kW for more than 24 h and at 90 kW for 1/2 h
LS version
TV version
SR RF

## Slide 15: CaCo: Cavity Combiner
Combine 2 IOTs
Filter Harmonics
Operation with faulty IOT
SR RF

## Slide 16: CaCo
SR RF
In routine operation, CaCo has performed reliably and without problems.

## Slide 17
Plunger for single IOT operation
(actuated with a piston)
80 kW operation in single IOT
SR RF
CaCo

## Slide 18
SR RF
CoStub: Coaxial shortcut using stub tunners
To isolate the not operational IOT for single IOT operation

## Slide 19
In operation
SR RF
CoStub
CaCo
CoStub
CoStub
Power after Costub AT 80 kW | 0.365 W
Initial/ final temperture of the stubs at 80 kW | 24ºC/26ºC
Arcs | Not detected
RF Leaks | Not observed
Power Reflected to the active IOT at 80 kW | 85 W

## Slide 20: Watrax: Waveguide to Coaxial transition
Allow water cooling channels in
Up to 160 kW
Fit the geometry
SR RF

## Slide 21: Watrax
Maximum CW power: 160 kW
VSWR: 1.061
Max. peak electric field: 239 kV/m
Power dissipated: 74.1 W
SR RF

## Slide 22
SR RF
Watrax: Power test at DESY
250 kW

## Slide 23
Alignment
Tension
Bead motion
Wire on which beads are attached
bead
RF cavity: DAMPY - HOM damped cavity
(in collaboration with Bessy)
CAVITY DAMPY
Type single-cell
Number 6
Frequency 500 MHz
Rsh 3.3 Mohm
SR RF
HOM damped RF cavity

## Slide 24
SR Dampy 01 to 06 Power tests
All cavities operate without problems
SR RF

## Slide 25
  Based on a commercial FPGA board (Lyrtech VHS-ADAC)
  Analog Front Ends for pre-processing of RF signals
  Amplitude, phase and tuning loops implemented
  Diagnostics and extra capabilities
Lyrtech Digital Board
Analog Front End
SR RF
Digital Low Level RF

## Slide 26
DLLRF Power test
Amplitude RMS Errors: 0.11% @ 80MHz
0.03% @ 1MHz
Tests at 75 kW
Phase RMS Errors: 0.05º @ 80MHz
0.02º @ 1MHz
SR RF

## Slide 27
Thank you
Conclusion
RF developments at ALBA:
  Cavity Combiner CaCo
  Coaxial Short-Switch CoStub
  IOT improvements LS-IOT
  HOM Damped Cavity Dampy
  Waveguide-Coax transition Watrax
  Digital LLRF DLLRF