## Slide 1: FEEDBACK SYSTEMS AT ALBA
DEELS’15
A. Olmos, U. Iriso (CELLS)
G. Rehm, M. Abbot (Diamond)

## Slide 2: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 3: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 4: FOFB – At a glance
88 BPMs and 88 H/V correctors distributed in 16 cells
Diamond Communication Controller protocol for data transfer
Distributed correction calculation on 16 non-real time CPUs
Ring type topology without redundancy links
MicroResearch timing boards recycled as position reading nodes (sniffers)
One XBPM (Libera Photon) integrated in the FOFB

## Slide 5: FOFB – At a glance
cPCI crate
IP modules
Libera
Libera
Libera
Libera
Libera
Libera
Libera
Libera
Next
sector
Previous
sector
PMC board
(sniffer)
CPU
Tx Board
Corrector PS
Tx Board
Corrector PS
Corrector PS
…
Corrector PS
One sector out of 16

## Slide 6: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 7: FOFB – In operation
No Slow Orbit Feedback
RF frequency control by standalone process
No Safe-stop, no BPMs check, no CC check
FOFB nonstop running from the 13th of May until last Friday
* No beam lost due to FOFB
* No phone-call about FOFB problems
Lucky?
Is all this really needed?

## Slide 8: FOFB – In operation
No Safe-stop, only limits on correctors setpoints:
- Max correctors delta 5mA
- Max correctors absolute 8A
No BPMs check:
- System always considers BPM data as “healthy data”
- No check on BPMs noise, FFT, glitches …
No Communication Controller check
- No on-line check of FOFB links
Correction problems will drive the PS to their Max –> beam lost
A failure in one Libera will run correctors to crazy values
Status after 24h
What should we consider as a failing link?
How does a CC error look like?
FOFB stays ON after a beam trip
Does this matter?

## Slide 9: FOFB – In operation

## Slide 10: FOFB – In operation
Good but … to be improved

## Slide 11: FOFB – In operation
But while doing this slides ...
Unknown problems with FOFB. Operation changed to only SOFB mode

## Slide 12: FOFB – In operation
FA data during the trip (10kHz)
5mm

## Slide 13: FOFB – In operation
FA data during the trip (10kHz)
?
1ms
5mm

## Slide 14: FOFB – In operation
5mm
1ms
5mm
Horizontal (mm)
Vertical (mm)
Time (ms)
Post-Mortem data during the trip (TbT – 1.1MHz)

## Slide 15: FOFB – In operation
5mm
50us
5mm
Horizontal (mm)
Vertical (mm)
Time (ms)
Post-Mortem data during the trip (TbT – 1.1MHz)
Post-Mortem data shows same pattern than when loosing beam because of RF trip (?)

## Slide 16: FOFB – In operation
FA data during the trip (10kHz)
Could this be when beam was already lost?
(rem: FOFB does not stop)
We have no means right now to time-correlate this FA data with the Post-Mortem data

## Slide 17: FOFB – In operation
BPMSR0903 after 2nd trip
BPMSR0906 after 3rd trip
More puzzling FA data
At some moment, w/o beam,
these BPMs had FA position jumping
between 2 fixed values (?)
And few seconds later they start
to recover “normal” data

## Slide 18: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 19: FOFB – Fast Archiver
System developed by Diamond and used at other facilities since 2011
Our current Fast Archiver consists of:
- a PCIe SPEC card as sniffer to the FOFB network (CC integration by Diamond)
- 1Tbyte HD in a desktop PC
- Capability to store 37h of 88 BPMs position data @ 10kHz
- Data can be retrieved from Matlab, Python Qt GUI or command line tools
We’ll soon upgrade to a 12Tbytes system in an IndustrialPC, allowing more than 2 weeks of data
Server with few HDs allowing many Tbytes of archived BPM data @ 10kHz rate
1Tb

## Slide 20: FOFB – Fast Archiver
Very useful diagnostics tools for FOFB commissioning and continuous fast BPM data monitoring
Live 10kHz BPM data analysis
Retrieve 10kHz data from archiver

## Slide 21: FOFB – Fast Archiver
FFT analysis allows localization of possible noise sources
BPMs data
Response Matrix
Correctors space
Horizontal
50Hz
Vertical
50Hz

## Slide 22: FOFB – Fast Archiver
Frequencies
below 50Hz
It’s time to hunt the guilty

## Slide 23: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 24: BbB – At a glance
Libera FrontEnd
Libera BbB
IFI 100W ampli
Hybrids
Button BPM
Stripline Kickers
100W atten
Scope

## Slide 25: BbB – At a glance
BPM
FFK - Y
FFK - X
BbB - Y
Timing
EVR
BbB - X
Clk2 - 500MHz
Clk1 - 500MHz
Xout
Yout
A
B
C
D
100W Att
100W Att
Load
Scope
Load
Scope
100W Att
100W Att
Load
Scope
Load
Scope
500MHz
ALBA Master Clock
RF FE
100W
100W
100W
100W
Hybrids

## Slide 26: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 27
Diamond colleagues offered a collaboration to port Diamond TMBF to ALBA system
Main tasks carried out (mainly by Diamond or under their advise):
* Migrate the full FPGA code from SystemVerilog to VHDL language
* Adapt it to ALBA machine (harmonic number, revolution frequency, tunes, …)
* Modify graphical interfaces (EDM) and side utilities (scripts) to make them work in
ALBA environment
* Install an “EPICS worm” (EPICS Base) inside our Tango control room
* Build libca library to transfer data to Matlab
* Permanently install Diamond TMBF code in our Liberas BbB (factory code washed)
* HW checks/modifications on Amplifiers, Hybrids and phase matching of cables
We did a not very successful try with I-Tech Matlab interface
TMBF Commissioning with beam in presence of G. Rehm and M. Abbot (May 11-12)
BbB – Diamond TMBF Commissioning

## Slide 28
Simple View GUI
Expert View GUI
BbB – Diamond TMBF Commissioning

## Slide 29
Phase Offset Optimization (Mixer)
RF FrontEnd X/Y outputs
Phase Clock Optimization (Sampler)
PhaseX=20deg @BBB-FE
PhaseY=-20deg @BBB-FE
PhaseX Clock: +20deg
PhaseY Clock: +60deg
Hor
Ver
BbB – Diamond TMBF Commissioning

## Slide 30
Single Pulse from Libera BBB + Ampli + Kickers + Attenuators
The amplis distort the signal, produces a ripple of ~6ns
We will kick adjacent bunches!
Single Pulse (2ns) from Libera BBB
BbB – Diamond TMBF Commissioning

## Slide 31
Synchronize BBB pulse with bunch passage (single bunch):
Add 1ns cable for exact matching
BBB Pulse
BBB Pulse
+ delay +
1ns cable
Bunch Passage
BbB – Diamond TMBF Commissioning

## Slide 32
Inject 100mA, uniform filling, chroms (1.6, 3.4)
Loop closed just by setting the vertical phase
We also reduce further the ChromV ~ 0, beam was kept stable
BbB – Diamond TMBF Commissioning

## Slide 33: Content
Fast Orbit Feedback
At a glance
In operation
Fast Archiver
TMBF Features
Bunch-by-Bunch Feedback
At a glance
Diamond TMBF Commissioning

## Slide 34: BbB – Diamond TMBF Features
Diamond TMBF allows to:
Setup different “Banks”: ways to act on the beam (damping, excitation, sweep…)
Combine them with the “Sequencer”
This can produce interesting features (see next, and also Guenther’s ppt at DEELS14 )

## Slide 35: BbB – Diamond TMBF Features
Get a stable beam using TMBF
Excite mode m
Measure the growth time
Switch TMBF back on for that mode
Measure damping time
Damp again mode m, and repeat for m+1
Unstable modes identification
Prepare the following sequence:

## Slide 36: BbB – Diamond TMBF Features
Unstable modes identification
Excitation Mode m
Growth rate, 1/turns
Damping
No Damping
RW
?

## Slide 37: BbB – Diamond TMBF Features
Bunch Cleaning:
Define a backwards sweep around Qv
Activate DAC only in buckets B77 & B80
Killed B76, B77
Killed B79, B80
Killed in previous tests
Before BC
After BC

## Slide 38: BbB – Diamond TMBF Features
Tune Measurement using PLL:
Measure beam phase response to an input (needs to be very close to Qv)
Keep track of frequency (tune) change to match phase
Input signal needs to be very small, compatible with normal operation
In this case, one measurement/200 turns
Applied only to bucket 60
DQ ~ 1e-5!

## Slide 39: BbB – Diamond TMBF Features
Frequency, Hz
FFT Amplitude
Measurement taken with ChromV~0
FFT of a BPM buffer of 2.5e5 turns
Tune Measurement using PLL:
Main tune jitter peaks at 100 and 300Hz
Compatible with tune jitter measurements with other means:

## Slide 40: BbB – Conclusions
Diamond TMBF has been commissioned at ALBA
Quite easy and straight-forward (thanks to Guenther and Michael!)
An “EPICS worm” has been installed in our Tango-based Control Room
Diamond TMBF allows several interesting features and already tested at ALBA:
  Sequences to identify unstable modes
  PLL tune tracking with 1e-5 precision
So far, only commissioned in the vertical plane due to hardware (ampli) failure.
Many thanks for your attention !!

## Slide 41: BBB – Extra slides

## Slide 42
Commissioning procedure
* Finding proper RF FE settings (phase offset, clock phase, …)
* Problem in Hybrids X signal
* BbB “brain washing” failed  processor board already reflashed at Diamond
* Ugly single pulse out of the amplifier. That will affect adjacent bunches
* 2ns jump of the single pulse out of one BbB unit. Diamond has reproduced the problem in their lab (DAC initialisation)
* Change ALBA timing to TMBF needs
* Aligning system to the bunches @ machine SBM
* Inject 100mA uniform filling beam
* Vertical loop closed just by setting the feedback phase
* Chrom reduced to ‘0’ and beam kept stable
* Bunch cleaning test:
- no bunch kicking until scrapper closed
- 2 bunches kicked out because of ampli
* Unstable modes identification (m=-8)
*
*

## Slide 43: Extra slides: 2ns jumps
Scope in persistence mode, to show the 2ns jump (green). The violet trace is the trigger.

## Slide 44: Extra Slides: ADC offsets
Fixed w.o. beam, just using the GUI capabilities