## Slide 1: SOLEIL diagnostics transverse projects and collaborations
Nicolas HUBERT#
on behalf of the SOLEIL Diagnostics group
# nicolas.hubert@synchrotron-soleil.fr
DEELS
15-16 June 2015
ALBA, Barcelona
Femto-slicing @ SOLEIL
Thom-X Project
COXINEL

## Slide 2: femto-slicing principle
[1] A.A. Zholents, Proc. of the PAC’07 Conference, Albuquerque, New Mexico, USA, 69-73 (2007).
From R. W. Schoenlein et al., Science 287, 2237(2000).
Schematic of a femto-slicing [1] experiment:
Production of femtosecond X-ray pulses at SOLEIL:

## Slide 3: SOLEIL specificities
SDC6
SDM8
SDM7
SDC7
SDM6
1) One single laser Ti:Sa 800 nm, 1 kHz, 30 fs-fwhm for the machine and for the CRISTAL beamline
dipole
Laser
Beam
Courtesy M-A. TORDEUX,
SOLEIL accelerator physics group

## Slide 4: SOLEIL specificities
Modulator
Wiggler
SDC6
SDM8
Laser
Beam
SDM7
SDC7
SDM6
2) Modulator = a wiggler used for femto-slicing and as a source for PUMA beamline
Wiggler Type | Hybrid out-vacuum
Magnetic period | 164.4 mm
Period number | 20
Magnetic gap | 14.5 mm – 240 mm
Magnetic components | Poles: VACOFLUX50 (Saturat. field: 2.35 T) Magnets: VACODYM 764 TP (magn.: 1.37 T)
Max. magnetic field | 1.81 T
PUMA BL
Courtesy M-A. TORDEUX,
SOLEIL accelerator physics group

## Slide 5: SOLEIL specificities
SDC6
SDM8
Laser
Beam
SDM7
SDC7
SDM6
Core
3 mm
Slice
Effective Dispersion
Deff (m)
S (m)
3) Slice separation using
the machine’s horizontal dispersion function
Modulator
Wiggler
Additional chicane to reduce the photon emission angle
Shifted diaphragm in BL frontend
Courtesy M-A. TORDEUX,
SOLEIL accelerator physics group

## Slide 6: SOLEIL specificities
Laser
Beam
CRISTAL
(U20)
TEMPO
(HU44 + HU80)
DEIMOS
(HU52 + HU65)
GALAXIES
(U20)
Modulator
Wiggler
4) Delivery to several beamlines:
2 « Phase 1 » beamlines (CRISTAL, TEMPO)
2 beamlines under study (DEIMOS, GALAXIES)
1 extra possible beamline ? (SEXTANTS)
75 fs
140 fs
80 fs
210 fs
Courtesy M-A. TORDEUX,
SOLEIL accelerator physics group

## Slide 7: Setup
Laser: 80 m transport line from CRISTAL Laser hutch to interaction point under primary vacuum
0 : Wiggler
DIAG_IR
DIAG_101
DIAG_01
DIAG_103
ENC104
ENC105
DIAG_20
DIAG_02
ENC103
ENC102
ENC101
LASER
Output
MgF2
DIAG_00
55 m
LASER ROOM
LENS 9 m
PUMA BL
MgF2
STORAGE RING ROOF
STORAGE RING TUNNEL
CRISTAL BL
EXPERIMENTAL HALL
DIAG_001
Wiggler
5 mirrors under x-y remote control
5 centering diagnostics
1 pointing diagnostic
Foreseen position feedback

## Slide 8
Extraction of the IR radiation:
IR diagnostics
Extraction mirror
towards PUMA beamline
Wiggler
e-
laser
laser + wiggler
Infra-Red Diagnostics: measure the overlaps between Laser and SR radiations
 inside the Storage Ring tunnel,
under the PUMA beamline frontend.
In Vacuum Cu Mirror
Saphhire Window
Filters
2.5 m Lens
Rmax Mirror
Conception : M. Labat

## Slide 9
IR diagnostics
towards PUMA beamline
Wiggler
e-
laser
laser + wiggler
Main constraint on the extraction mirror:
 Pwigg= 250 W @ 10 mA
Extraction mirror
Extraction of the IR radiation:
Conception : M. Labat, D. Zerbib, J-L. Marlats

## Slide 10
IR diagnostics
Mirror
Extraction mirror
towards PUMA beamline
IR diagnostics
Wiggler
e-
laser
laser + wiggler
Transport of the IR radiation:
Conception : M. Labat, D. Zerbib, J-L. Marlats

## Slide 11
IR diagnostics
IR detectors :
    For temporal overlap:
     Fast photodiode (FPD 310-FV from Menlo)
    For spatial overlap:
     Optics + CCD (Basler) for imaging in the wiggler
    For spectral overlap:
     Spectrometer (Ocean Optics USB2000)
Conception : M. Labat

## Slide 12: Alignment in the Wiggler of SR and laser (in focused mode and low power)
Wiggler entry
1 pixel on the CCD ≡ 20 µm in the transverse plane of the wiggler
Wiggler middle
Wiggler exit
SR
Laser

## Slide 13: Synchronisation
  Measure arrival time of the SR on the photodiode, without laser.
  Add filters, open the laser shutter, adapt the optical fiber to equal SR and laser intensity level.
  Measure arrival time of the laser, adjust the laser delay to equal the SR’s.
  Final resolution: 10 ps
SR
Laser
1 ns

## Slide 14: THz Diagnostics
fs pulses  CRISTAL BeamLine
Wiggler
Laser
PUMA BeamLine
THz pulses extracted @ AILES beamline
fs pulses 
TEMPO BeamLine
Evaluates the dip in the core beam using the THz beamline AILES
    High sensitivity measurements:
    Bolometer
    QMC 1 ms, SAI card
    IR Labs 1.7 µs, oscillo Lecroy 1GHz
Fast measurements (turn by turn):
    THz diode
    Virginia Diode Virginia 1 nsdiodes)
10 m
-1 0 1
Time (ps)
1
0
-1 0 1
Time (ps)
1
0

## Slide 15
Bolometers:
  1st bolometer :
    Used during the first 2 tests of interaction
    Bolometre from QMC
    Time response = 1 ms
    ->> Integration of the signal : 1 coherent shot + 1000 incoherent shots
    (Laser @ 1 kHz, SR @ 846 kHz)
    Acquisition with SAI Card (@500 kHz max)
  2nd bolometer :
    Used during the third succesfull test of interaction
    Bolometre from IR Labs
    Time response = 1.33 µs
    ->> Integration of the signal : 1 coherent shot + 1 incoherent shot
    ->> Much more suitable for first (not optimized) THz detection
    “Acquisition” with Oscilloscope LeCroy (1 GHz)
THz diagnostics

## Slide 16: First results : THz intensity measurement
1st turn
2nd turn
3rd turn
4th turn
  After a rough optimisation, we saw some signal up to 4 turns with the fast diode (0.3 – 0.5 THz BW).
1 kHz trigger
Bolometer signal = Interaction !!
  With the bolometer (0.1 – 3 THz BW), we saw a few V signal at laser repetition rate.
  Bolometer signal
  Fast diode signal

## Slide 17: Femto-slicing summary
  Slicing interaction is done (since 29/09/2014)
Setup is very reproducible (2 hours to set up the slicing operation)
Bolometer operation is painful, to be replaced by photodiode soon
  First photons seen on CRISTAL Beamline the 09/02/2015
Toward user operation
  First experiments on CRISTAL planned in the 2nd part of 2015
  Preparation for next beamlines: TEMPO (2015), DEIMOS, GALAXIES, SEXTANTS

## Slide 18: The ThomX Project
What is ThomX?
  Light source based on Compton Back Scattering effect (CBS)
    Most efficient energy amplifier
    Production of hard X-rays with relatively low energy machine
    Example : 50 MeV electrons and 1.23 eV laser give up to 50 keV back scattered X-rays
  High average flux
    Storage ring to have a high repetition rate
    high average power laser amplified in a Fabry Perot resonator
Target : Store one electron bunch of 1 nC over 20 ms in the ring
Store one laser pulse of 25 mJ in the FP cavity
==> Thom-X is a demonstrator
=> 1013 Ph/s

## Slide 19: The ThomX Project
What is ThomX?
  Collaboration!
  Supported by
    the EQUIPEX program – French Research Ministry,
    Ile-de-France region,
    CNRS-IN2P3
    Université Paris Sud XI
SOLEIL has in charge the design of the accelerator and will be part of the installation tests and commissioning

## Slide 20: ThomX Machine
Laser
and FP cavity
Cycle Frep = 20 msec
RF pulse length 3 s
Energy 50 - 70 MeV
Easy integration
2 Interaction Points in the arcs
Frees the straight sections
X-rays
RF gun 3 GHz
Linac 3 GHz 50-70 MeV
Linac dump
& diag
E-diag
Matching section
Inj & Ext section
Interaction point
Feedback system & RF 500 MHz
Ring dump
10 m.
7 m.

## Slide 21: ThomX: what for?
Transfer of the SR techniques to these new machines. Many fields can be interested…
At present two contributors: Medical field (ESRF, INSERM Grenoble) Cultural Heritage (C2RMF CNRS – Louvre Museum)
Painting analysis
K-edge imaging (Pbwhite, Hg vermilion…) of a Van-Gogh’s painting
J. Dik et al., Analytical Chemistry, 2008, 80, 6436
Paleontology
Non-destructive analysis
Physiopathology and Contrast agents,
Dynamic Contrast Enhancement SRCT
Convection Enhanced Delivery =>Stereotactic Synchrotron RT
Imaging,
Mammography
Microtomography
  J Cereb Blood Flow and Metab, 2007. 27 (2):292-303.
Journal of Radiology 53, 226-237 (2005)
Biston et al, Cancer Res 2004, 64, 2317-23
Thanks to G.Le Duc, P.Walter

## Slide 22: Expected beams characteristics
Injector | 
Charge | 1 nC in 1 bunch
Laser wavelength and pulse power | 266 nm, 100 J
Gun Q and Rs | 14400, 49 MW/m
Gun accelerating gradient | 100 MV/m @ 9.4 MW
Normalized r.m.s emittance | 8  mm mrad
Energy spread | 0.36%
Bunch length | 3.7 ps
Ring | 
Energy | 50 MeV (70 MeV possible)
Circumference | 18 m
Crossing-Angle (full) | 2 degrees
Bx,y @ IP | 0.2 m
Emittance x,y (without IBS and Compton) | 3 10-8 m
Bunch length (@ 20 ms) | 30 ps
Beam current | 17.84 mA
RF frequency | 500 MHz
Transverse / longitudinal damping time | 1 s /0.5 s
RF Voltage | 300 kV
Revolution frequency | 16,7 MHz
Harmonic Number | 30
x @ IP (injection) | 78 mm
Tune x / y | 3.4 / 1.74
Momentum compaction factor c | 0.013
Final Energy spread | 0.6 %
Laser and FP cavity | 
Laser wavelength | 1030 nm
Laser and FP cavity Frep | 36 MHz
Laser Power | 50 – 100 W
FP cavity finesse / gain | 30000 / 10000
FP waist | 70 m
Source | 
Photon energy cut off | 46 keV (@50 MeV), 90 keV (@ 70 MeV)
Total Flux | 1011-1013 ph/sec
Bandwidth | 1 % - 10%
Divergence | 1/ ~ 10 mrad without diaphragm @ 50 MeV

## Slide 23: ThomX Diagnostics
Position
  Mechanics:
    Linac: 1 stripline
    Transfer Line: 4 striplines
    Ring: 12 buttons BPMs
  Electronics:
    Libera Brilliance +
      First unit delivered in January
      Series to be delivered end of September

## Slide 24: ThomX Diagnostics
Feedthroughs
  All provided by PMB-ALCEN (France)
  90 Buttons, identical to ESRF ones (Φ=10,8 mm)
    Ordered in may 2015
  25 Feedthroughs for striplines are on the same basis, button replaced by a long central pin.
    Ordered in January 2014
    Delay + Major difficulties to be in tolerances
    Loss of concentricity during transportation?

## Slide 25: ThomX Diagnostics
Charge
  Linac and transfer line:
    3 Bergoz in-flange ICTs
  Ring:
    BPM Sum Signal
Transverse Feedback
  Design of the stripline
Ion Cleaning (mandatory!)
  Use of 20 additional BPM buttons for polarization
Loss (LAL in charge):
  Optic fibers (Cherenkok radiation)
Bergoz in-flange ICT
FBT Stripline

## Slide 26: ThomX Diagnostics
Diagnostic stations (LAL in charge)
  4 screens on a translation stage
    1 YAG(Ce) screen in all stations
    1 optical transition radiation (OTR) screen in all stations
    1 target to allow an online calibration of the camera in all stations
    one Cerenkov screen for bunch length measurements in station DS2 (described in more detail below).
  Measurements:
    Transverse size (YAG + OTR)
    Emittance (Q-scan + screen)
    Energy (Dipole + screen)
    Length (Cerenkov + Streak Camera)
Diagnostic station x5

## Slide 27: ThomX Diagnostics
Bunch length measurement
  Sources
    End of Linac: Cerenkov radiation
    Storage ring: Synchrotron radiation
  Complex transport path for the photon beam
    13 mirors (3 motorized)
    7 lenses
  Detector: Streak Camera
    Hamamatsu
    Already delivered and tested

## Slide 28: ThomX schedule
Machine will be installed in an already existing building
Infrastructure works (utilities, shielding) should start in september 2015
Installation is foreseen at the end of 2016
Commissioning planned for begining 2017
~2 years delay on initial planning

## Slide 29
www.lunex5.com
Improve the performances and reduce the size/price of the FEL sources:
LWFA
- solid basis for the study of advanced FEL lines
- evolution towards high repetition rate
- evolution towards a multi-user FEL facility
- FEL seen as an application qualifying the LWFA
- compact / Lab. scale
- «high risk», «challenging»
- low repetition rate (1 Hz)
- fiability of the operation?
400 MeV Superconducting Linear Accelerator
400 MeV Laser WakeField Accelerator
Advanced FEL line
266 nm
HHG
40-20 nm
Pilot user experiments
The LUNEX5 project
Superconducting linear accelerator
LUNEX5 project layout

## Slide 30
www.lunex5.com
ERC Advanced Grant COXINEL
COherent X-ray source INferred from Electrons accelerated by lasers
COXINEL ( Advanced) aims at demonstrating Free Electron Laser amplification with present LWFA performances with a existing TW laser.
Objectives :
• demonstrate an appropriate transport to the undulator
• demonstrate FEL amplification at 200 nm and at shorter wavelength (40 nm)
• investigate and control (theory/experiments) FEL performance (seeding, polarisation...)
Acknowledgments to ERC Advanced Grant COXINEL (340015) M. E. Couprie

## Slide 31
www.lunex5.com
COXINEL general integration
Dump
Stripline
Spectrometer
Mechanical conception : D. Zerbib, K. Tavakoli, J. L. Marlats
Chicane
Quadrupoles
Steerer
Undulator
String PM Quad
~10 m

## Slide 32: Charge monitors
Measuring the beam charge: up to 10 pC!
Use of 2 Bergoz in-flange Turbo-ICT
ICT location
Beam axis
www.lunex5.com

## Slide 33: Position monitors
Measuring the beam position with (very) good resolution (few µm) at low charge (10 pC)
Use of 16 mm cavity BPMs from Swiss FEL
Mounted on translation stage
CBPM location
Beam axis
Study of a resonant stripline in parallel
www.lunex5.com
B. Keil, “Design of the SwissFEL BPM System”, IBIC13

## Slide 34: Tests on SOLEIL TL1
Charge and position monitors have been installed on SOLEIL TL1 for testing in January 2015:
www.lunex5.com

## Slide 35: Tests on SOLEIL TL1: charge
Turbo-ICT: sub pC resolution
ICT1
ICT2
T-ICT
DCCT (Booster)
Beam charge measurement comparison on SOLEIL first transfer line and booster
www.lunex5.com
10 pC

## Slide 36: Tests on SOLEIL TL1: cavity BPM
Pickup:
Analog signals from CBPM
Centering CBPM
Electronics:
  Web server running on the electronics
    Permits preliminary tests
  Dedicated Tango server is under development
    Mandatory for machine correlated measurements
www.lunex5.com

## Slide 37: Transverse size monitors
Aim:
  Image the beam along the experiment for alignment and beam size measurement
Principle:
  Screen on the beam path
  Imaging system of the screen with variable magnification
Screens location
Beam axis
www.lunex5.com

## Slide 38: Transverse size monitors
Screen:
  3 different screens mounted on a translation stage
  YAG and LyCo : scintillator screens for high flux / low resolution measurements
  Metallic screen: OTR screen for higher resolution measurement. But COTR effects ?
Imaging system:
  5 lenses telescope
  2 lenses mounted on a stage to provide 2 magnifications (large field and high resolution)
e- beam
d0
d1
d2
d3
d4
d5
F0
F1
F2
F3
F4
F1
F2
www.lunex5.com

## Slide 39: Transverse size monitors
Preliminar design:
Screens on the motorized stage
for insertion on the beam path
Imaging system
(G=1.1 – 0.2 for 5 microns resolution and 20mm field of view)
www.lunex5.com

## Slide 40: Conclusion
SOLEIL diagnostic group is involved in 3 very interesting but time and resources demanding projects:
  Femto-slicing
  ThomX
  Coxinel
Without forgetting the SOLEIL operation!
  29 Beamlines taking beam
  450 mA Hybrid
  490 mA full ring (500 mA expected this summer)
  Simultaneous operation of IDs on canted straight section (see MEA talk)
Thank you for your attention!