## Slide 1
Status of Metrology Light Source
Jörg Feikes, Ji Li on behalf of MLS team
Helmholtz-Zentrum Berlin, Germany

## Slide 2
Outline
The Metrology Light Source(MLS)
Problems in operation
Status of Robinson Wiggler Project
Single-particle effects limiting the bunch length in low alpha mode

## Slide 3
Circumference Revolution time | 48 m, 160 ns = 1/6.25MHz
Injection Energy | 105 MeV
Operational Energy beam current | 50 MeV to 630 MeV 1pA (1e-) – 200mA
Momentum Comp. Factor | -0.05 < α < 0.05
Emittances at 630 MeV | 25 nmrad (low emittance) 120 nmrad (standard user) 250 nmrad(low alpha)
Typical lifetimes in different operation modes | standard 6h @150mA, 100h@1pA low emit. 2h @150mA low Alpha 10h @150mA
BESSY II
Metrology Light Source (MLS)
U125 undulator
RF cavity, HOM damped
500 kV@ 500 MHz, h=80
Owned by PTB
Run by HZB
The Metrology light source

## Slide 4: Problems
  Occasional water leaks
    Power supply room, 01.2019
      caused by corroded water-cooled sextupole power supplies
      5 out of 7 PS corroded (21 same PS at BESSY II run well for 20 years, same cooling water quality)
      we decided to replace all of them with air-cooled PS
      air-cooled PS running well since Sep.2019
    On MLS bunker roof, 09.2019
      caused by improperly designed water flow controller
      All of them have been replaced
  An IOT failed due to vacuum leak, 08.2019 (after 12000 h)
    replaced by a formerly installed IOT
    a new IOT ordered

## Slide 5: Problems
  Power cut caused by disfunction UPS
    Electric network fluctuation in 07.2019
    Misoperation when repairing the UPS in 08.2019
  Venting of the MLS storage ring in 10.2019

## Slide 6
current*Lifetime/mA*h
beam current/mA
1100
50
200
0
1
2
3
5
4
6
7
09/10/2019
09/11/2019
1. MLS storage ring completely vented by operational error
2. pumping
3. beam scrubbing
4. user operation for last urgent measurement before baking
5. access to bunker – activation of all NEG-coated chambers located in the straight sections
6. beam scrubbing
7. user operation with reduced performance
8. user operation at nearly full performance
8
1 week
Problems

## Slide 7
Field on the mid plane of one period of the Robinson Wiggler
manipulating damping partition D
  smaller emittance and larger energy spread
  smaller transverse beam size
  longer bunch length
together with maintained transverse beam size by excitation
  large bunch volume
  increasing Touschek lifetime (~ 200%)
Robinson Wiggler

## Slide 8
Analytic expression of 3D field
Vector potential(Ax, Ay, Az)
Hamiltonian
Symplectic integrator for solving Hamiltonian Equations:
Complex asymmetric field in RW:
Modified Halbach expression
Symplectic Runge-Kutta intergrator
Generating function method
Tracking Result:
- Dynamic Aperture is OK
- operating the RW in the MLS SR is possible
Symplectic tracking for Robinson Wiggler

## Slide 9
internal report: „Potential and risks of installing a Robinson Wiggler at the MLS”
  based on the discussion in PTB steering committee meeting.
  Potential:
    to gain a factor of 2 in Touschek lifetime after a long installation and commissioning period
    more options for lattice development
  Price:
    a 10 weeks shut down for installation + long commissioning time
    partly venting of the storage ring  months to recover
  Risks:
    small dynamic aperture due to manufacture errors
    influence on injection caused by residual magnetic field of the RW
  Conclusion: It is not desired to invest now.
  What to do now?
    summarizing the work done for publication and final report
    options for a future machine with a Robinson Wiggler (MLS II)
What have we gained in this project?
  a complete Ph.D. Thesis (Tobias Tydecks)
  knowledge in magnet design, power supply, magnetic material….
  modeling the insertion devices for linear optics and nonlinear dynamics study
    analytic expression for complex field
    symplectic integrator
Robinson Wiggler Project: officially cancelled for now

## Slide 10
‘The First Experiment towards Steady-State MicroBunching’
Xiujie Deng(Tsinghua University, Beijing, China) tomorrow
Why MLS?
Low alpha approach for SSMB
MLS: optimized for low alpha operation in design stage
Sufficient commissioning time available.
Successful SSMB PoP experiment at the MLS
laser pulse
laser modulator to form optical buckets like RF buckets
Microbunching for high power + steady state for high repetition rate
Proposed by A. Chao and D. Ratner
On-going investigation in Tsinghua University, Beijing, China
PoP at the MLS Phase I: One-pass experiment
principle of Steady-State MicroBunching(SSMB)

## Slide 11
Verification of single-particle effects driven by PoP experiment of SSMB:
longitudinal quantum radiation excitation (partial alpha effect)
second order transverse-longitudinal coupling
in collaboration with Xiujie Deng, Alex Chao et. al (Tsinghua University, Bejing)
and Roman Klein, Arne Hoehl (PTB, Berlin)
Single-particle effects limiting the bunch length in low alpha mode

## Slide 12
Bunch Length Limit 1: fluctuations of partial alpha
A stochastic fluctuation of where the photo emission takes place produces a fluctuation of path length of one revolution [1]:
quantitatively described by variance of (s) = partial alpha
this introduces additional energy spread and bunch lengthening
∝ Variance of {(s)} ≈ in standard low alpha mode @MLS
in a special low alpha lattice
This means: while lowering and shortening bunches to σ < 1 ps
the energy spread increases notably
confirmed at the MLS with Compton Back Scattering measurement
[1] Shoji, Yoshihiko, et al. "Longitudinal radiation excitation in an electron storage ring.“ Physical Review E54.5 (1996):R4556
[2] Deng, et al, .“Experimental Verification of the Longitudinal Quantum Radiation”, to be submitted to soon
CBS photo spectra measurement with Synchrotron frequency of 18 kHz, 5 kHz and 2.5 kHz [2]
Energy spread widening with decreasing alpha value [2]
[2]

## Slide 13
Bunch Length Limit 2: second order transverse-longitudinal coupling
a non-zero amplitude betatron oscillation lengthens the beam path length in the second order
also confirmed at MLS with Compton Back Scattering measurement
one of several papers submitted

## Slide 14
Bunch distribution distorted from Gaussian :
Bunch Length Limit 2: second order transverse-longitudinal coupling

## Slide 15
Thanks for your attention!
Thanks to all the contributions from HZB and PTB colleagues !

## Slide 16: Backup slides 1: First order transverse-longitudinal coupling
[1] C. Tang, et al, .“AN OVERVIEW OF THE PROGRESS ON SSMB”, proceedings of FLS2018, Shanghai, China
[2] Shoji, Yoshihiko. "Bunch lengthening by a betatron motion in quasi-isochronous storage rings.“ Physical Review Special Topics-Accelerators and Beams7.9 (2004): 090703
Particles with different Betatron amplitudes and phases pass bending magnets on different trajectories, resulting in longitudinal displacement differences and a bunch length limit: [1][2]

## Slide 17: Backup slides 2: Modified HalBach formula *
* J. Li, et al, .“SYMPLECTIC TRACKING FOR THE ROBINSON WIGGLER”, proceedings of IPAC19, Melbourne, Australia

## Slide 18: Backup slides 3: SymPLeCtic RUNge-Kutta integrtator
[1] A. Wolski, Beam dynamics in high energy particle accelerators. London, UK: Imperial Colleague Press, 2014.

## Slide 19: Backup slides 4: Numerical generating function method
[1] M. Scheer, “Beschleunigerphysik und radiometrische Eigenschaften supraleitender Wellenlänenschieber”,Ph.D. thesis, Mathematics and Nature Sciences Dept., Humboldt-Universität zu Berlin, Berlin,Germany,2008