## Slide 1
G.Baranov, A.Bogomyagkov, V.Bukhtiarov, S.Gurov, G.Gusev, K.Karyukina, V.Kiselev, A.Krasnov, G.Kulipanov, V.Kuzminykh, A.Levichev, E.Levichev, P.Logachev, N.Mezentsev, I.Morozov, I.Okunev, P.Piminov, Y.Rakshun, T.Rybitskaya, V.Shkaruba, S.Sinyatkin, M.Skamarokha, A.Starostenko, A.Tribendis, A.Tsyganov, N.Vinokurov, P.Vobly, A.Zhuravlev, K.Zolotarev, I.Zubavichus et.al.
SKIF  Fourth generation synchrotron light source in Novosibirsk

## Slide 2
Russian acronym SKIF (Siberian Circular Photon Source) also means Scyth or Scythian. Scythians were ancient nomads originally located in northern Black Sea and fore-Caucasus regions.
Scytho-Siberian culture attributes to the population inhabited modern Altai Republic (south of Novosibirsk), which were known as skilled crafts gold workers. Altai kurgans – large burial mounds – provides many samples of beautiful gold works, and we believe that our new synchrotron light source will shine as bright as Scythian jewelries.

## Slide 3
Formal motivation
08.02.2018 during his visit to Novosibirsk V.Putin supported development of Siberian synchrotron light source SKIF
Instruction of President of Russia, May 7, 2018, paragraphs 1b and 4.
Decree of President of Russia, #204, April 18, 2018.
Governmental Executive Order #2659-p, December 1, 2018.
Scientific Council headed by the Vice Prime Minister T. Golikova approved SKIF specs and location in November 2019.
Governmental Decree opening the project financing is expected in December 2019.
Government together with Presidential council of science and education must develop the full range of measures to build 4th generation light sources in Protvino and Novosibirsk Akademgorodok.
V.Putin
18.04.2018

## Slide 4
Informal motivation
Novosibirsk Akademgorodok (Academic town) consolidates more than 40 research institutes in physics, chemistry, biology, medicine, condensed matter, geology, etc. and most of them have expressed their interest in new facility
BINP has great experience in development, production, study and maintenance of large accelerator facilities including synchrotron light sources
Siberian Synchrotron and Terahertz Radiation Center consists of several dozen of research groups with more than 40 years of experimental experience
Novosibirsk State University and Novosibirsk Technical State University will secure new scientific center with young but skilled staff
Institutes of Akademgotrodok
Novosibirsk State University
Novosibirsk State Technical U.

## Slide 5
Beam energy 3 GeV
Circumference < 500 m
Natural horizontal emittance 100 pm (zero current, zero coupling, no IDs)
Injection complex à la NSLS II (150-200 MeV linac and full energy booster synchrotron)
Well proven top-up off-axis injection in the horizontal phase space with four-kicker bump, etc.
Transverse DA for injection Axinj  7 mm (with errors and misalignments)
Momentum DA for good Touschek lifetime with strong IBS (p/p)max  ~2.5%
Sufficient number of beamlines
  From wigglers and undulators (straight sections)
  Hard X-ray from strong field dipoles
  Soft X-ray and VUV from weak field magnets
Robust, effective, low price, fast development design
Specifications

## Slide 6
20 км
15 км
BINP
SKIF
Novosibirsk
Novosibirsk Int. Airport
SKIF locates in technopolis Kol’tsovo
Green field. No interference with other enterprises
Quiet area free from heavy industry
Electrical power substation is nearby
Almost equal distance from both downtown and Akademgorodok
Location

## Slide 7
Е = 3 GeV
Imax = 400 mA
x = 75 pm (0 mA, no IDs)
C = 476 m
16 SS (14 for IDs)
Configuration
Traditional and common configuration:
Injector linear accelerator with maximum energy 200 MeV
Small size booster synchrotron with maximum energy 3 GeV and orbit length 158.7 m
Electron storage ring 16-fold symmetry with 3 GeV energy and 476 m circumference

## Slide 8
Basic cell (soft X-ray beamline)
SX
QXB
SX
QXB
SY
SY
BQY
TME/FODO cell 3.49 m in length with reflection symmetry
SX: focusing chromatic sextupole (2300 T/m2)
QXB: focusing quadrupole (51 T/m) moved over 4.6 mm outward to produce –3.6 mrad anti-bend
SY: defocusing chromatic sextupole ( –2300 T/m 2)
BQY: bending magnet (0.55 T) with low defocusing gradient (–7.7 T/m)
Drifts between elements are enough to accommodate BPMs, flanges, bellows, etc.

## Slide 9
Modified cell (hard X-ray beamline)
SX
SX
SY
SY
QXBM
QXBM
BQYM
BQYM
BHF
High field dipole BHF is inserted inside modified BQY.
QXBM: focusing quadrupole (49 T/m) moved over 7.3 mm outward to produce –5.4 mrad anti-bend
BQYM: bending magnet (0.64 T) with low defocusing gradient (–10.1 T/m)
BHF: high field (2.1 T) short (7 cm) zero gradient permanent magnet dipole producing hard X-ray radiation
The modified cell replaces the middle cell in every other lattice super-period, giving 8 hard X-ray beamlines from bending magnets.

## Slide 10
6 m
x/ y=13/1.9 m
6-m-long dispersion-free straight section with two quadrupole doublets (double doublet or DD section) accommodates undulators, relatively low field wigglers (~4.5 T 50 mm period 2 m long wiggler does not increase but decrease emittance), injection and RF equipment.
Beta_y* is low enough to suppress optic distortion caused by insertion devices. Beta_x* is large enough for traditional injection with horizontal bump of stored beam.
High x straight section
Disp.
supp.
Disp.
supp.
Cell
Cell

## Slide 11
4.24 m
x/ y=0.7/3.5 m
Low x straight section
Strong field (7-8 T) wigglers/shifters being installed in the high x section may increase the beam emittance. To prevent it a low x section is designed by installing 2 additional quadrupoles (double triplet or DT section).
Only gradients in the straight section are changed slightly. All other magnets are identical to the DD-section solution.
Disp.
supp.
Disp.
supp.
Cell
Cell

## Slide 12
Super-periods
DT-solution
LS 6m
LS 6m
LS 6m
LS 6m
LS 6m
HFM 2.1T
SS 4.24m
LFM 0.5T
LFM 0.5T
HFM 2.1T
DD-solution

## Slide 13
Lattice type: 7B Achromat
Symmetry: 16 (DD sections) or 8 (DT sections), TBD
1 straight section for main RF, 1 straight section for injection and 3hRF, 14 straight sections for IDs
Linac 2856 МГц/8 = 357 MHz
Synchrotron 158.76 m (harmonic number 189)
SKIF 158.76 m х 3 = 476.14 m (harmonic number 567)
14 beamlines from wigglers and undulators
8 hard X-ray beamlines from 2.1 T magnets (can be increased up to 16 if necessary)
8 soft X-ray beamlines from 0.52 T magnets (can be increased up to 16 if necessary)
In total, there are 46 beam lines
Parameters and features
Beam energyt | 3 GeV
Circumference | 476.14 m
Revolution period | 1.59 µsec
Symmetry | 16DD (or 8DD/8DT)
Horizontal emittance | 75 pm·rad
Energy spread | 9.44·10-4
Energy loss/turn | 499 keV
Betatron tunes (x/y) | 51.43 / 17.59
Natural chromaticity (x/y) | -151 / -59
Harmonic number | 567
RF frequency | 357 MHz
RF voltage | 0.75 MV
RF acceptance | 2.59 %
Synchrotron tune | 1.21·10-3
Partition number () | 2.05 / 0.95
Damping time () | 9 / 20 ms
Straight section length | 6 m
Straight section length No | 16 2 for RF and injection 14 for IDs
Beam energyt | 3 GeV
Circumference | 476.14 m
Revolution period | 1.59 µsec
Symmetry | 16DD (or 8DD/8DT)
Horizontal emittance | 75 pm·rad
Energy spread | 9.44·10-4
Energy loss/turn | 499 keV
Betatron tunes (x/y) | 51.43 / 17.59
Natural chromaticity (x/y) | -151 / -59
Harmonic number | 567
RF frequency | 357 MHz
RF voltage | 0.75 MV
RF acceptance | 2.59 %
Synchrotron tune | 1.21·10-3
 | 2.05 / 0.95
 | 9 / 20 ms
Straight section length | 6 m
Straight section length No | 16 2 for RF and injection 14 for IDs

## Slide 14
Квадруполь
30 мм
70 Т/м
300 А х 10 витков
8 mm SR gap
4D DA
Nonlinear beam dynamics was carefully studied with MAD-X, Accelerator Toolbox and two in house accelerator development codes. Correspondence is very good.
MAD-X On-energy transverse dynamic aperture for two families chromatic sextupoles in the cells.
DD lattice, observation in the middle of the straight section.
Particles stable for 2048 turns. Here and below x = 13 m, y = 1.9 m
Ax = -10… +12 mm
Ax = -10… +12 mm
Ay = 3.5 mm

## Slide 15
Квадруполь
30 мм
70 Т/м
300 А х 10 витков
8 mm SR gap
Betatron tunes vs. amplitude
Betatron tunes as a function of the amplitude for both planes and for both DD and DT configurations.

## Slide 16
Квадруполь
30 мм
70 Т/м
300 А х 10 витков
8 mm SR gap
Momentum aperture and bandwidth
Main RF on (V1 = 0.75 MV), 3hRF on (V3 = 0.18 MV) providing threefold bunch lengthening. 10000 turns.
Dynamic acceptance (RF off)
Tune bandwidth
dP/P  -4… +2.6 %
dP/P  -4…+6 %
dP/P  2.5 %
Dynamic acceptance (RF on)

## Slide 17
Horizontal aperture map
Tunes selection (per super-period)
Color indicates the horizontal DA in mm (left DT, right DD)

## Slide 18
Vertical aperture map
Color indicates the vertical DA in mm (left DT, right DD)

## Slide 19
Energy aperture map
Color indicates the energy acceptance in % (left DT, right DD)

## Slide 20
Dynamic aperture conclusions
Only two families of chromatic sextupoles in the cells provide reasonable dynamic aperture (transverse and longitudinal).
The aperture, decreased by the lattice errors (linear and nonlinear), is still sufficient for good Touschek lifetime (including IBS) and traditional robust injection with a horizontal bump.
There is room in the dispersion suppression section for additional multipole correctors to optimize the DA or/and bandwidth but it is not evident if it is really needed.

## Slide 21
s=5.1 mm
s=15.3 mm
VRF=752 kV
Nb=510
= 10%
E/E = 2.6%
s=5.1 mm
s=15.3 mm
VRF=752 kV
Nb=510
= 10%
E/E = 2.6%
Multi-bunch mode (510 bunches):
I = 400 mA (0.783 mA/bunch, 7.77109 е/bunch). Betatron coupling = 10% (y  9 pm  r at c= 1 Å).
A threefold bunch elongation by the 3rd harmonic RF provides 7 h Touschek lifetime and x0= 67 pm  xIBS= 93 pm.
Intra beam scattering (bare lattice, DT)

## Slide 22
Intra beam scattering (2 wigglers)
For users we planned to install two SC multipole wigglers (B0 = 4.5 T, 0 = 5 cm, Lw = 2 m) in the DD straight sections. The betatron function is optimized; therefore, the wigglers effectively reduce the emittance.
4.2 T, 5 cm, 2 m wiggler for Australian Light Source, N.Mezentsev
Flat beam, max brightness
(Quasi) round beam, max lifetime

## Slide 23
=5 см В = 4.5 Т Nper=20 L = 2 m
1 wiggler: 75 pm  63 pm
2 wigglers: 75 pm  56 pm
Wigglers and emittance
Emittance
Energy spread
Partitions

## Slide 24
y/y25%
DA w/o wiggler correction
Wiggler optics distortion
=5 см В = 4 Т Nper=20 L = 2 m
Only local (triplet) correction
K1_qm12: 4.8147  4.7703 m-2
K1_qm13: +6.5620  +5.9983 m-2
K1_qm11: 0.5036  +0.5574 m-2
x=0.01 y=0.001
Wiggler and lattice
Before optics correction
After optics correction

## Slide 25
Preliminary 2D simulation did not show any showstoppers in the magnets design and production. 3D detailed simulation is ongoing.
Magnets
Sextupoles
Quadrupoles
Dipoles
Name | L, m | S,T/m2 | Smax, T/m2 | Ø, mm | N
SY | 0.25 | 2314 | 2500 | 34 | 160
SX | 0.3 | 2351 | 2500 | 34 | 64
SXH | 0.15 | 2351 | 2500 | 34 | 32
Name | L, m | B,T | G, T/m | Gmax, T/m | ,mrad | Ø, mm | N | Comment
Q1 | 0.25 | - | 57 | 80 | - | 30 | 16 | Long straight section
Q2 | 0.25 | - | 60 | 80 | - | 30 | 15 | Long straight section
Q3 | 0.25 | - | 2 | 80 | - | 30 | 16 | Short straight section
Q4 | 0.25 | - | 62 | 80 | - | 30 | 16 | Short straight section
Q5 | 0.25 | - | 76 | 80 | - | 30 | 16 | Short straight section
BD2 | 0.15 | -0.15 | 49 | 60 | -2.21 | 36 | 32 | Dispersion suppressor Reverse bend
BD | 0.15 | -0.24 | 51 | 60 | -3.56 | 36 | 144 | Low field magnet cell Reverse bend
BDI | 0.15 | -0.36 | 49 | 60 | -5.41 | 36 | 16 | High field magnet cell Reverse bend
Name | L, m | B,T | G, T/m | ,mrad | Gap, mm | N | Comment
BF | 1.30 | 0.55 | -7.689 | 71.29 | 30 | 72 | Regular cell, low field magnet
BF2 | 0.65 | 0.59 | -2.033 | 38.29 | 30 | 32 | Dispersion suppressor
BFI | 0.47 | 0.64 | -10.132 | 30.16 | 30 | 32 | High field magnet side bend
BI | 0.07 | 2.10 | 0.000 | 14.66 | 30 | 8 | Permanent high field magnet

## Slide 26
High Field Magnet
1
2
3
4
L= 0.1 m
Bmax = 2.11 T
Iw/coil = 10 kA.
1 – Steel M1200-100
2 – NdFeB, 1.43T, permanent magnet
3 – NdFeB, 1.24T, permanent magnet
4 – Permendur;
Permanent magnet with peak field of 2.1 T

## Slide 27
Low field magnet
There are two types of the low field gradient magnets:
L = 1.3 m, B = 0.55 T, G = -7.7 T/m (regular cell dipole)
L = 0.47 m, B = 0.64 T, G = -10.1 T/m (side bend for the 2.1 T magnet)
Both are similar to these for NSLS II booster synchrotron
Booster NSLS II magnets

## Slide 28
Shifted quadrupole (reverse bend)
Parameters:
G = 55 T/m L = 0.15 m
R= 18 mm Iw/coil = 8 kA

## Slide 29
Quadrupoles & Sextupoles
Quad. parameters:
G= 67 T/m
(Gmax =80 T/m)
L = 0.25 m
R= 15 mm
Iw/coil = 6.4 kA
Chart: I, A/mm2
| 3 | 5 | 8.6999999999999993 | 10 | 13
 | 20.92 | 34.95 | 60.2 | 67.27 | 78.85
Sext. parameters:
S= 2500 T/m2
L = 0.25 m
R= 17 mm
Iw/coil = 7 kA

## Slide 30
Injection
Injection is from the booster-synchrotron similar to NSLS II with 4-kicker horizontal bump.
BINP has experience in design and production of 3 GeV booster.
Energy, GeV | 0.15 | 3
Periods | 4 | 
Circumference, m | 158.76 | 
Repetition, Hz | 1 | 
Hor. Emittance, nm | 0.17 | 37
 | 0.4 | 30
 | L(m) | Fi(mrad) | Н(Т) | U(кV)
Kick1 | 0.25 | 3.1 | 0.124 | 40
Kick2 | 0.25 | 2.1 | 0.084 | 27
Kick3 | 0.25 | 2.1 | 0.084 | 27
Kick4 | 0.25 | 3.1 | 0.124 | 40
Sep1 | 0.4 | 30 | 0.75 | 
Sep2 | 1.4 | 200 | 1.43 | 

## Slide 31
Injection
Axinj  8 mm
First three turns: 0 – injected beam in the septum, 1-3 – after the 1-3 turns respectively.
Axinj  8 mm  98% inj.efficiency
Axinj  7 mm  87% inj.efficiency
We have 2-3 mm of the aperture margin for errors and misalignments.
Further optimization is available.
0
1
2
3
Septum d = 2 mm
Injection tracking with nonlinearities and radiation

## Slide 32
FEL at SKIF for EUV lithography
Extreme ultraviolet lithography (EUV or EUVL) is a next generation lithography technology using a range of extreme ultraviolet (EUV) wavelengths, roughly spanning a 2% FWHM bandwidth about 13.5 nm.
We plan to install at SKIF Free Electron Laser based on a 6 m SC helical undulators to develop and study EUV lithography. The average power of about 50-100 W can be reached.
Undulator parameters
Power density for the 1st harmonic
Radiation ring at 30 m distance

## Slide 33
3D view

## Slide 34
– ESRF-EBS, 4 m CPMU18
– ESRF-EBS, 4.8 m U35
– ESRF-EBS, 3.2 m U42
– ESRF-EBS, 1.6 m W150
SKIF, 4 m SC Undulators, λu = 15.6 mm, B= 1.2 T
SKIF, SC Wigglers, λu = 50 mm, B= 4.2 T
Ring parameters:
1 – ESRF-EBS (ESRF-EBS Design Report,Fig.8.1, p.278):
E= 6GeV, Ibeam= 200 mA
εx = 147 pm*rad
εy = 5 pm*rad
2 – SKIF:
E= 3GeV, Ibeam= 400 mA
εx = 75 pm*rad
εy = 7.5 pm*rad

## Slide 35
We have a basic design of the Novosibirsk 4th generation light source SKIF (3 GeV, 476 m, 70 pm @zero current and  = 10%).
For nominal multibunch current 400 mA, IBS increases emittance to 90 pm with 7 hours of the Touschek lifetime and 17 mm bunch length (RF3 on).
16 straight sections (14 are for IDs) of two types: 6 m (x = 13 m, y = 1.9 m) for injection, RF and undulators and 4.24 m (x = 0.7 m, y = 3.5 m) for strong field wigglers.
30 beam lines are foreseen: 14 are from IDs, 8 high field permanent magnets (2.1 Т) and 8 from regular cell magnets (0.5 Т).
Transverse DA is sufficient for traditional, simple and effective injection. Longitudinal aperture/bandwidth provide good Touschek lifetime. Only two sextupole families are used.
Magnet types are minimized for the cost and production time saving.
Free electron laser for EUV lithography study will be installed at SKIF enhancing its experimental capability
Conclusions