## Slide 1: Present Undulator Activities at DESY
Markus Tischer, on behalf of the DESY ID group
27th European Synchrotron Light Source (ESLS) Workshop
27-29 November 2019 at ALBA Synchrotron, Barcelona

## Slide 2: Undulator-Installations at DESY
FLASH1 SASE IDs (6)
sFLASH Seeding-Undulators (4)
FLASH2 SASE Undulators (12)
PETRA III Undulators (22)
PETRA III Damping-Wigglers (20)

## Slide 3: Outline
1 Introduction
2 APPLE III Undulators
  Design
  Status
3 Variable Period Undulators
  Concept
  Design route, pre-prototype tests

## Slide 4: Planar Undulators
Planar Magnet Structures
  Virtual shimming by 4 screws
  Individual pole shift and tilt
  Continuous adjustment (~2µm)
  Fast tuning, 2m device ~1day per iteration
Magnet module design reworked
Support mechanics in different lengths
Revolver Mechanics
  design completed (2.5m)
  2 or 3 different magn. structures (sase, modulator or chicane)
(T. Ramm et al. Proc. MEDSI 2018)

## Slide 5: APPLE-III with Force Compensation
e-
Longitudinal Shift / mm
-8 -5 0 5 8
Vert., Horiz. Force / period [N]
400
0
-400
-800
  Force reduction up to factor of ~8
  “Continuous” correction magnet signature ~1%
  Same magnets for force compensation  improved sorting
  Measurement with a normal bench through 1mm side gap
  Customized Hall probe holder
solid: with compensation dashed: without comp.
for FLASH2 Afterburner, FLASH2020+ and ~PETRA IV

## Slide 6: APPLE-III Transverse Field Dependence
Circular mode
gap=1
gap=6
gap=19
longitudinal
vertical
horizontal
vertical
horizontal position
Curvature (~y2) vertical as function of gap
horizontal
By – vertical
Bz - horizontal
-10 0 10
-10 0 10
-1 0 1
-1 0 1
1 5 10 15
B0(gap)
Curvature (~z2) horizontal as function of gap
Symmetric configuration at minimum gap
Focusing effect of vertical field
  for all gaps
De-/Focusing of horizontal field
  depending on gap

## Slide 7: APPLE-III Transverse Field Dependence
Circular mode
longitudinal
vertical
horizontal
vertical
horizontal position
zoomed in
By – vertical
Bz - horizontal
-10 0 10
-10 0 10
-1 0 1
-1 0 1
1 5 10 15
B0(gap)
Curvature (~z2) horizontal as function of gap
1 5 10 15
1 5 10 15
Symmetric configuration at minimum gap
Focusing effect of vertical field
  for all gaps
De-/Focusing of horizontal field
  depending on gap
  ~”friendly” within the useful gap range
gap=1
gap=6
gap=19
0.4 0.2
0
Curvature (~y2) vertical as function of gap
0
0

## Slide 8: APPLE-III Forces
Forces on a single keeper
  relevant for keeper and brackets
  considered case: λU = 16mm
  A+B magnet pair on 1 keeper
  ~85N / +-45N (long. / transversely)
Forces of a full row
  relevant for design of shift drive
  considered case: λU = 32mm
  vertical/horiz. ~2100N per 1m
  very small dependence on shift
  long. ~900N per 1m (inclined mode)
Moments
  considered case: λU = 32mm
  a few ~100Nm per 1m on each quadrant (work in progress…)

## Slide 9: APPLE-III Keeper Design
Present design parameters (prelim.)
  Period length 16mm, magn. gap Ø 8mm
Various design studies
  Magnet clamping
  Correction magnet rotation
Next steps:
  Keeper prototypes
  Verify stiffness, tuning, operability

## Slide 10: APPLE-III
Further development points:
  Shift drive
  Adaption to gap mechanics
  Magnetic measurement tools, procedures
First full device:
  FLASH2 Afterburner
  Serves as full scale prototype for the FLASH2020 seeding IDs

## Slide 11: Outline
1 Introduction
2 APPLE III Undulators
  Design
  Status
3 Variable Period Undulators
  Concept
  Design route, pre-prototype tests

## Slide 12: Variable Period Undulator
Present Developments – Variable Period Undulator
Concept : Arrangement of cylindrical magnets (Pavel Vagin)
Varying the angle between two neighbor magnets results in period change
Common rotation changes field amplitude or phase
Amplitude, phase or period adjustments are more or less orthogonal to each other
Ongoing DESY development
Synch. Rad. News 31:3 (2018) 48-52; SRI2018, AIP Conf. Proc. 2054, 030024 (2019)

## Slide 13: Variable Period Undulator
Present Developments – Variable Period Undulator
Concept : Arrangement of cylindrical magnets (Pavel Vagin)
Varying the angle between two neighbor magnets results in period change
Common rotation changes field amplitude or phase
Amplitude, phase or period adjustments are more or less orthogonal to each other
Ongoing DESY development
Synch. Rad. News 31:3 (2018) 48-52; SRI2018, AIP Conf. Proc. 2054, 030024 (2019)

## Slide 14: Spectral Performance
PETRA parameters
Halbach PPM, magnets 50mm x 50mm x λu/4
VPU, magnets ⌀10mm x 10mm
Same length, same 10mm gap, 6GeV

## Slide 15: Spectral Performance
PETRA parameters
With circular aperture and crossed VPU(a) horizontal and vertical fields sum up 
Dividing VPU in two independent halves along the beam(b)  variable period APPLE-II

## Slide 16: FEL SASE Performance
FLASH parameters

## Slide 17: Mechanical Design
friction bearing
ball bearing
Ball bearing
  Less friction and play
  Smooth rotation
Friction bearing
  Stiffer, less bending
  Simpler, more economic
Harmonic drive
  Direct mounting
  Maybe just a test…
H. Bolat, P.Vagin

## Slide 18: Mechanical Design
Various items to test or improve
  Glueing of magnet to the shaft
  Manufacturing tolerance of axis
  Stiffness of coupling
  Backlash or hysteresis
  Integration of encoders
Small prototype
Stretched wire measurements of the individual magnets in the long structure

## Slide 19: Angular Positioning Error
Assume: 2m VPU with 200 magnets of ⌀10mm, each randomly dispositioned by ±0.5̊
Random error of ±0.5̊ of each magnet results in phase error of less than 3̊ rms, for 2m device, and trajectory distortion is within the oscillation amplitude.
Single ⌀10x10mm magnet field integral is 1.3Tmm/rad, 0.5 degree angular error corresponds to 0.01Tmm = 10Gs*cm

## Slide 20: Angular Positioning Error
Backlash error caused by magnetic forces is not random, but also periodic => much lower phase and field integral errors
Other ”static” errors like magnetization direction or mechanical positioning errors could be measured and compensated by software correction of the magnet angle.
- Magnetic field - Force - Torque

## Slide 21: Rotary Encoder
Rotary transformer
AMR magnetic rotary encoder
First preliminary test:
  Noise level ~2mrad (~0.1°)
  strange nonlinearity probably due to misalignment of sensor vs magnet, but ratio shows a clean tan-signal
sin
cos

## Slide 22: Inductive Rotary Encoder
1 -
0 -
-1 -
x 100
http://www.ti.com/sensing-products/inductive-sensing/overview.html
4-channel inductive sensor for LDC1614
Radial or axial arrangement
Noise level <0.1̊ deg (~1kHz)
Enhanced resolution

## Slide 23: Variable Period Undulator – Conclusion
Software-defined magnetic field
Variable Period Undulators provide a wider wavelength range
Quasi-periodic, Figure-8, Transverse Gradient undulators, …
Arbitrarily shaped magnetic field: dipoles, phase shifters, multipoles, …
Lower magnetic field amplitude/K => lower intensity of high harmonics
Simpler support structure
Reliable operation of lots of drives
Complex control software
Integral magnetic measurement methods
Embedded automatic “shimming”

## Slide 24: Thank you!

## Slide 25: Multipoles
(a, b, c) Quadrupole up to 90T/m
(d) Sextupole up to 8kT/m^2
(e) Octupole up to 2MT/m^3

## Slide 26: Transverse Gradient Undulator
Disabling only left (or right) part of structure produces transverse gradient undulator with dK/K/dx ~ 0.2/mm

## Slide 27
Markus Tischer
DESY, FS-US
markus.tischer@desy.de
+49 40 8998 2923

## Slide 28: Backups

## Slide 29: Magnetic Measurement Equipment
Local field distribution
  12m measurement bench
  Hall probes (1D, 3D), pickup-coils
  Pulsed wire
Field integral probes
  Stretched wire
  Moving coil
Calibration tools
  NMR-probe in spectrometer magnet for calibration of Hall probes
  Interferometer, Touch probe as a mechanical 3D-measurement probe
Touch probe measurement of
pole contour

## Slide 30: Tuning
vert. dipole hor. quadrupole hor. dipole vert. quadrupole
Chart: Trajectory initial
Chart: Trajectory tuned
  Phase error < 1deg
  Off-axis trajectory correction (remove quadrupoles)

## Slide 31: Phase Shift Without Trajectory Offset
9th
3rd
1st harm.
Notes: large figure: undulator radiation for different harmonics – emitted radiation
and how they are affected by an induced phase step due to a local field modification
no traj. offset

## Slide 32: Mechanical Design of Local Phase Shifter
cylindrical magnet
stepper motor with gearbox
rotary encoder
coupling

## Slide 33
Variable Period Undulators
Variable period permanent magnet helical undulator. J. Mun, Y. Jeong, N. Vinokurov, K. Lee, K. Jang, S. Park, M. Jeon, S. Shin, Phys. Rev. ST Accel. Beams 17, 2014
Variable period undulators as synchrotron radiation sources. G. Shenoy, J. Lewellen, D. Shua, N. Vinokurov,
J. Synchrotron Radiat. 10, 205 (2003).
Modeling and designing of variable period and variable pole number undulator.
I. Davidyuk, O. Shevchenko, V. Tcheskidov, N. Vinokurov, Phys. Rev. Accel. Beams 19, 2016
The highly adjustable magnet undulator.
M. Hamberg, FEL2015, TUP057
Previous and recent developments