## Slide 1: ALBA II Accelerator Design Francis Perez (thanks to the ACE team)
ALBA II Day June, 30th, 2021

## Slide 2: Present lattice

## Slide 3: Constrains
Keep beam energy 3 GeV
Keep the tunnel  SR with similar compact circumference
Keep existing ID beamlines  preserve 16 cells and source points
Bending beamlines can be relocated
Keep injector (present εxbooster = 10 nm∙rad)
Keep infrastructures, as much as possible
Straight sections 4 m, with βx βy 2 m
Reduce emittance by more than a factor 10 (<400pmrad)

## Slide 4: Proposed solution
From 2 x 8 double-bend lattice (DBA)
To 1 x 16 multi-bend lattice (6BA)

## Slide 5: Proposed solution
Main (preliminary) parameters

## Slide 6
The 6BA lattice 4 fold symmetry
At ID position, with 100% coupling, almost round beam:
sx = 14.0 um s’x = 7.1 urad
sy = 15.1 um s’y = 6,6 urad
High beta required for Injection
1/4
At ID position, today:
sx = 127 um ; s’x = 47 urad
sy = 5.2 um ; s’y = 4,4 urad

## Slide 7: Implementation

## Slide 8
Straigth sections for IDs
308 mm
308 mm
308 mm
But 3 will be used for
the Accelerator:
1 for Injection
2 for RF
With high betas (bx=11,7 ; by=10,0)

## Slide 9
Straight | BL |  | Comments
SR01 | 2 | FREE | 
SR02 | 4 | MSPD | 68mm displacement
SR03 | 6 | XAIRA | 
SR04 | 8 | FREE | 308mm displacement / Large Beta
SR05 | 11 | NCD | 
SR06 | 13 | XALOC | 68mm displacement
SR07 | 15 | FREE | 
SR08 | 17 | RF | & Pinhole3
SR09 | 20 | LOREA | 
SR10 | 22 | CLAESS | 68mm displacement
SR11 | 24 | CIRCE | 
SR12 | 26 | RF | 
SR13 | 29 | BOREAS | 
SR14 | 31 | FAXTOR | 68mm displacement
SR15 | 33 | FREE | 
SR16 | 0 | INJECTION | 
4x FREE
9x IN USE
3x MACHINE
ALBA2 - Straight Sections

## Slide 10: Brilliance comparison for three relevant ALBA IDs
IVU XAIRA EPU LOREA SCW MSPD

## Slide 11: Bending beamlines
0,73 T
1,02 T
1,02 T
1,02 T
1,02 T
0,73 T
The 6BA lattice has a lower bending field than ALBA (1,4 T)
11
We propose to replace
few of them by:
Brasilian
SIRIUS
Ligth Source

## Slide 12
Superbend: 3.2 T combined permanent magnet
Influence in the emittance:
less than 10%
if high field peak is short and at the center.

## Slide 13
Bendings emission comparison
1 T
3.2 T
For beamlines Eph ≲ 4 keV
the 1T bending is more favorable
1,02 T
at middle
1,02 T
at end
3,2 T
at middle

## Slide 14
BM | BL |  | Super Bend | Comments
SR02_QD_3 ? | 1 | MIRAS |  | 
SR02_QD_1 | 3 | FREE | Ok | 
SR03_QD_1 | 5 | FREE |  | Limited space due to MSPD
SR04_QD_2 | 7 | FREE |  | 
SR05_QD_1 | 9 | MISTRAL |  | 
 | 10 | Blocked |  | NCD
 | 12 | Blocked |  | Xaloc
SR07_QD_2 | 14 | FREE |  | 
SR08_QD_2 | 16 | NOTOS | Ok (-2.5º) | Superbend requires to move BL 480mm
 | 18 | Blocked |  | Truck entrance
SR09_QD_4 | 19 | FREE | Ok | 
 | 21 | Blocked |  | CLAESS – Used for Pinhole2
SR11_QD_2 | 23 | FREE |  | 
SR12_QD_2 | 25 | MINERVA |  | 
 | 27 | Blocked |  | eALBA
SR13_QD_3 | 28 | FREE | Ok | 
SR14_QD_4 | 30 | FREE | Ok | 
SR15_QD_4 | 32 | FREE | Ok | 
 | 34 | Blocked |  | Pinhole1 + Xanadu
9x FREE
4x IN USE
6x BLOCKED
ALBA2 - BM beamlines

## Slide 15: Possible sources
13 IDs
  12 low betas
  1 high betas
12 bendings
  Keep the bending beamlines MISTRAL & MINERVA with 1T bending
  Move NOTOS to a 3,2T bending
  4 more possible with 1T bending
  5 more possible with either 1T or 3,2T bending
MIRAS
  Could be maintained in the same position, but the mechanical design of the extraction from the SR has to be investigated.

## Slide 16: Possible long beamlines at BL02-ID , BL03-Bend, BL04-ID, BL08-ID

## Slide 17: Some questions
Movement of BLs?
  MSPD, XALOC, CLAESS and FAXTOR need to move 68mm.
  NOTOS will need to move 480mm, with a 3,2T bending.
Beam current?
  300 mA, 6 RF cavities, 2 straight needed  13 IDs
  400 mA, 8 RF cavities, 3 straights needed  12 IDs
eALBA?
  Space is reserved for the Electrons at ALBA proposal.
  It takes Experimental Hall space, the space not used of the injection, plus one possible bending beamline.

## Slide 18: Some (preliminary) conclusions
ALBA II seems feasible:
  emittance ∼ 150 - 200 pmrad
  betas X,Y ∼ 2.0 - 2.5 m
Up to 26 beamlines are feasible:
  13 IDs
  12 Bendings
    Some of these bending positions can be used for 3,2T superbend.
  1 IR (MIRAS)
The actual beamlines positions can be preserved, including the bending beamlines. But 4 x IDs and 1 x BM will need realignment.

## Slide 19: Thanks

## Slide 20: Beam sizes at emission points